## Slide 1
Program
MineOperate Technical Level 1
Machine Guidance
HP Shovel
JIGSAW version Fixed Offset
Edgar Sepulveda
Global Technical Manager, MineOperate
Date 02/24/2023
Version 1.6

## Slide 2: Purpose
This session shows …
At the end of this module, you will:

## Slide 3: Machine Guidance - HP Shovel
Hardware and sensors
2 Wi-Fi antennas
2 GPS antennas
1 Chassis inclinometer
1 Boom inclinometer
1 Stick inclinometer
1 Bucket inclinometer
1 Footswitch

## Slide 4: Machine Guidance - HP Shovel
Configuration
Find the HP Shovel product templates xml file in
    /opt/Jigsaw/xml/product_templates/

## Slide 5: Machine Guidance - HP Shovel
Configuration
Load HP Shovel product templates using xml file running xml_loader Tool
    /opt/Jigsaw/Tools/xml_loader -database jmineops /opt/Jigsaw/xml/product_templates/ lgs_apac.j2shovel.core+smart.xml

## Slide 6: Machine Guidance - HP Shovel
Configuration
Check product template groups.

## Slide 7: Machine Guidance - HP Shovel
Configuration
Change device name to star with client initials.

## Slide 8: Machine Guidance - HP Shovel
Configuration
Add new device group to each HP Shovel using the same hardware.

## Slide 9: Machine Guidance - HP Shovel
Configuration
Add new device group to each HP Shovel using the same hardware.

## Slide 10: Machine Guidance - HP Shovel
Configuration
Add group configuration to JSPanel application for the new device name.
Update high_precision_groups configuration for the new device name, Value must be equal to Device name.

## Slide 11: Machine Guidance - HP Shovel
Calibration
Add an Equipment Geometry record for the HP Shovel Equipment Type.

## Slide 12: Machine Guidance - HP Shovel
Calibration
Add an Equipment Geometry record for the HP Shovel Equipment Type.

## Slide 13: Machine Guidance - HP Shovel
Calibration
Add Geometry Points records for each Geometry Segments for HP Shovels.

## Slide 14: Machine Guidance - HP Shovel
Calibration
Add Geometry Segments records for each HP Shovel.

## Slide 15: Machine Guidance - HP Shovel
Calibration
Take X, Y and Z measurements.

## Slide 16: Machine Guidance - HP Shovel
Calibration
Add measurements to Geometry Segments records for the HP Shovel.

## Slide 17: Machine Guidance - HP Shovel
Calibration
Add an Equipment Geometry record for the HP Shovel Equipment Type.

## Slide 18: Machine Guidance - HP Shovel
Calibration
Add an Equipment Geometry record for the HP Shovel Equipment Type.

## Slide 19: Machine Guidance - HP Shovel
Calibration
Add Geometry Points records for each Geometry Segments for HP Shovels.

## Slide 20: Machine Guidance - HP Shovel
Calibration
Add Geometry Segments records for each HP Shovel.

## Slide 21: Machine Guidance - HP Shovel
Calibration
Take X, Y and Z measurements.

## Slide 22: Machine Guidance - HP Shovel
Calibration
Add measurements to Geometry Segments records for the HP Shovel.

## Slide 23: Machine Guidance - HP Shovel
Calibration
Chassis Inclinometer.

## Slide 24: Machine Guidance - HP Shovel
Calibration
Chassis Inclinometer.

## Slide 25: Machine Guidance - HP Shovel
Accuracy Test
Tool position

## Slide 26: Machine Guidance - HP Shovel
Accuracy Test

## Slide 27: Machine Guidance - HP Shovel

## Slide 28: Machine Guidance - HP Shovel - Questions

## Slide 29: Machine Guidance - HP Shovel - Answers

## Slide 30
Thank you.
Notes: Thank you.