## Slide 1
Program
MineOperate Technical Level 1
Machine Guidance
HP Shovel
NAV version Bucket Position
Edgar Sepulveda
Global Technical Manager, MineOperate
Date 02/24/2023
Version 1.6

## Slide 2: Purpose
This session shows …
At the end of this module, you will:

## Slide 3: Machine Guidance - HP Shovel
Hardware and sensors
2 Wi-Fi antennas
2 GPS antennas
1 Chassis inclinometer
1 Boom inclinometer
1 Stick inclinometer
1 Bucket inclinometer
1 Footswitch

## Slide 4: Machine Guidance - HP Shovel
Configuration
Find the HP Shovel product templates xml file in
    /opt/Jigsaw/xml/product_templates/

## Slide 5: Machine Guidance - HP Shovel
Configuration
Load HP Shovel product templates using xml file running xml_loader Tool
    /opt/Jigsaw/Tools/xml_loader -database jmineops /opt/Jigsaw/xml/product_templates/ lgs_apac.j2shovel.core+smart.xml

## Slide 6: Machine Guidance - HP Shovel
Configuration
Check product template groups.

## Slide 7: Machine Guidance - HP Shovel
Configuration
Change device name to star with client initials.

## Slide 8: Machine Guidance - HP Shovel
Configuration
Add new device group to each HP Shovel using the same hardware.

## Slide 9: Machine Guidance - HP Shovel
Configuration
Add new device group to each HP shovel using the same hardware.

## Slide 10: Machine Guidance - HP Shovel
Configuration
Add group configuration to JSPanel application for the new device name.
Update high_precision_groups configuration for the new device name, Value must be equal to Device name.

## Slide 11: Machine Guidance - HP Shovel
Calibration
Copy gpsLeica configurations and update device.

## Slide 12: Machine Guidance - HP Shovel
Calibration
Add GPS antennas measurements in gpsLeica configurations for each HP Shovel.

## Slide 13: Machine Guidance - HP Shovel
Calibration
Add tool measurements for each HP Shovel.
- uncrossedArmGeom_shovel
- uncrossedArmGeom_excavator
- fixedOffsetGeom

## Slide 14: Machine Guidance - HP Shovel
Geometry Measurements Pre-Survey Steps
Take Photos
  Take side-elevation photos of the shovel and send them to a HP specialist to mark-up and show which points are required.
Verify that the inclinometers are working.
  The RAW values need to be captured at the same time when the survey is done.
Provide surveyor with the required list of survey points
  Refer to JS01-03-12ED.xlsx (J2shovel Survey Data Entry spreadsheet)
  It is strongly advisable to discuss the list of points with the surveyor in order to clarify any uncertainties they may have.
Provide surveyor with ‘Surveying Tips’ PDF
  Refer to JS01-03-06 Appendix A.pdf

## Slide 15
Geometry Measurements While Surveying the Shovel
Take Photos
  Take side-elevation photos of the shovel while it’s parked up and being surveyed. This will help the HP specialist to perform some sanity checks on the calculated angles.
Capture the RAW values for each of the inclinometers
  Physically inspect each sensor and confirm whether facing LHS or RHS.
Assist the surveyor to shoot the points
  Make sure that the labels for each point are correct to avoid confusion.
Populate the ‘Survey Data Entry’ sheet and send to HP specialist to process.
Machine Guidance - HP Shovel

## Slide 16: Machine Guidance - HP Shovel
Geometry Measurements Processing the Surveying Points
The list of survey points should be provided to a HP specialist who is familiar with the process of converting the points.
  The calibration spreadsheet only produces output suitable for JGpsLeica configs.
  Manual conversions will need to be performed to calculate the geometry_segment data for non JGpsLeica systems.

## Slide 17: Machine Guidance - HP Shovel
Geometry Measurements - Face Shovel Entering the Geometry Measurements into MineOps
JGpsLeica version uses the configurations table.
Non-JGpsLeica version uses the geometry_segments table
  Values expressed in centimeters
Module | Attribute | Value
gps/gpsLeica | uncrossedArmGeom | isShovel=1 toolMountPositionDx=0.0 toolMountPositionDy=0.8 toolMountPositionDz=5.5 boomLength=8.0 stickLength=5.0 bucketLength=3.5 bucketWidth=3.0 bucketDepth=3.0 useDogBone=0

## Slide 18: Machine Guidance - HP Shovel
Inclinometer Calibration Calibrating the inclinometers (assuming lengths are already known)
  The PINK cells need to have data entered
  The BLUE cells are the calculated actual angles (based on the TPS measurements).
  The YELLOW cells represent the output for both the JGpsLeica and non-JGpsLeica versions.

## Slide 19: Machine Guidance - HP Shovel
Accuracy Testing Example Sign Off Sheet
  The results for the accuracy tests need to be recorded as evidence that the J2shovel system was accurate.
  The calibration parameters (eg. Measurements and sensor offsets) are also captured so that we have a complete set corresponding to the test results.
  The sign-off sheet should be provided to the site representatives and also saved into Hexagon’s repository of calibrations.

## Slide 20: Machine Guidance - HP Shovel
HP Shovel TRM
Hardware Training Level 2 Manual
  https://confluence.hexagonmining.com/download/attachments/53775489/Leica%20Hardware%20Level%202%20Training%20Manual%20v1.2.pdf?version=2&modificationDate=1476076699762&api=v2
J2shovel Survey Data Entry
  http://abrisrvfis02:81/Mining/Project%20Engineering/Jigsaw%20System%20Documentation%20Project/JS01%20-%20Products/JS01-03%20-%20DigNavJS/JS01-03-12ED%20-%20DigNavJS%20Survey%20Data%20Entry.xlsx
Shovel Inclinometer Recalibration
  http://abrisrvfis02:81/Mining/Project%20Engineering/Jigsaw%20System%20Documentation%20Project/JS01%20-%20Products/JS01-03%20-%20DigNavJS/JS01-03-15ID%20-%20j2Shovel%20Sensor%20Recalibration.xls
Register of J2shovel Calibrations
  http://abrisrvfis02:81/Mining/Project%20Engineering/Jigsaw%20System%20Documentation%20Project/JS01%20-%20Products/JS01-03%20-%20DigNavJS/Site%20Calibrations/JS01-03-10ID%20-%20DigNavJS%20Register%20of%20Calibrations.xls

## Slide 21: Machine Guidance - HP Shovel - Questions

## Slide 22: Machine Guidance - HP Shovel - Answers

## Slide 23
Thank you.
Notes: Thank you.