## Slide 1
Program
MineOperate Technical Level 1
OP Pro 2.8-005, 3.1-001
New Display support
Nathan George
Product Manager – OP Pro
Date: 07/31/2023
Version: OP Pro 3.1-001

## Slide 2: Agenda
New display hardware (D9S2-B X900)
OP Pro Release Plan
2.8-005 x64 applications and architecture
64 bit Multi-Application System Embedded Platform (MASEP)
New onboard software configuration & installation process

## Slide 3
Nathan George
Product Manager – OP Pro
Overview

## Slide 4: Display Replacements
Current Generation
CrossControl Display 9
D9S2-A
Next Generation
D9S2-B
CrossControl X900
D12S1-A
D12S4-A
CrossControl XM2
Motium MP1225
9” Range
12” Range
Display 9
EOL Notice
PL9_ECN_011
31-Oct-2022

## Slide 5: New Displays – OP Pro Release Support
Phase 3
Phase 2
OP Pro 2.8-005
MASEP 3.3.x
JSPanel x64 LP
OP Pro 2.8-005
MASEP 3.3.x
JSPanel x64 HP (Orenav)
JSPanel x64 HP (OreNav)
OP Pro 4.0
MASEP 3.3.x
JSPanel x64 LP
JSPanel x64 HP (Orenav)
Shell App x64 LP
JSPanel x64 HP (OreNav)
Phase 1
Not Supported

## Slide 6: New Displays - OP Pro Release Plan
OP Pro 2.8-005
- JSPanel x64 LP
OP Pro 2.8-005
JSPanel x64 LP
JSPanel x64 HP
OP Pro 4.0
JSPanel x64 LP
JSPanel x64 HP
Shell App x64 LP
Target Release Date
Available
31-Jan-2023
20-Mar-2023
20-Mar-2023

## Slide 7: OP Pro 2.8-005 x64 Onboard Architecture
Platform 2.26
OpenVPN
Platform 2.26
SQLite
JAMS
JSPanel LP x32
Current State
OP Pro 2.8-003/004
D9S2-A Display 9
Core LP
Intel Atom E3826 CPU
Dual Core 32 bit
Intel Atom E3845 CPU
Quad Core 32 bit
Future State
OP Pro 2.8-005
MASEP 3.3.x
OpenVPN
Platform 2.26
SQLite
JAMS
JSPanel LP x64
D9S2-B X900
Core LP
Intel Atom E3845 CPU
Quad Core 32 bit
Intel Atom x5-E3940 CPU
Quad Core 64 bit
Questions?

## Slide 8
Oey She Khun
Product Engineer - MineOperate
Installation & Configuration

## Slide 9: Overview
Overview
HxGN MineDiscover Display9 Series 2: D9S2-B (X900)
As of December 2022, the D9S2-A screen (Display9) is no longer available from the supplier due to the lack of availability of some components.
The D9S2-B screen (X900) is being provided as a replacement:
The D9S2-B screen is NOT a drop-in replacement for the D9S2-A due to the different software to be installed on it.
The D9S2-B screens cannot run the 32bit platform software (e.g.v2.26.x) and must instead use the 64bit MASEP platform. This limitation prevents the older 32bit applications (e.g.OP Pro) running on the D9S2-B screen.

## Slide 10: HxGN MineDiscover Display9 Series 2: D9S2-B (X900)
Hardware
Front view
Rear view

## Slide 11: HxGN MineDiscover Display9 Series 2: D9S2-B (X900)
Connectors – Comparison with Display9 Series 1
Symbol (Connector) | Connector | D9S2-A | D9S2-B
X1 | Power | Yes | Yes
X2 | CAN 2 | No | Yes
X3 | Ethernet 1 in D9S2-A, Ethernet 2 in D9S2-B | Yes | Yes
X4 | Ethernet 2 in D9S2-A, Ethernet 1 in D9S2-B | Yes | Yes
X5 | CAN 1 | No | Yes
X6 | AUX | No | Yes
X7 | USB 1 | Yes | Yes
X8 | USB 2 | Yes | Yes

## Slide 12: HxGN MineDiscover Display9 Series 2: D9S2-B (X900)
Resources
Change Notification
  PL9_ECN_011 - HxGN MineDiscover Display 9 - D9S2-A Replacement
Technical Reference:
  DxS2-x Hardware Variants
Data Sheet:
  HxGN MineDiscover Display 9 Data Sheet
  HxGN MineDiscover Display12 Data sheet
User Reference Manual:
  HxGN MineDiscover Display User Reference Manual
System, Subsystem and Cables Diagram:
  PL9_SUB_001C - 874206 - Screen MineDiscover 9
  PL9_SUB_052 - 874207 - Screen Power Input

## Slide 13: MASEP Platform
What Hardware Devices use MASEP
Article Number | Hardware Device Name | Device Description | MASEP version | Comments
 | D9S2-A | Display9 from Cross Control | v3.3.3 | 
C000147-53 | D9S2-B | X900 from Cross Control | v3.3.3 | 
 | D12S4-A | MPP1225 from Motium | v3.3.x | In Development
C000154-38 | D10S5-A | V1000 from Cross Control | v3.3.3 | 
 | D9S6-A | DisplayX-9 from Hexagon | v3.4 | In Development
https://confluence.hexagonmining.com/display/TR/MASEP+TRM+-+What+Hardware+Devices+use+MASEP

## Slide 14: MASEP Platform
MASEP
MASEP is an acronym for 'Multiple Application Supported Embedded Platform’ with primary purpose to allow multiple applications to co-exist on the common hardware.
Current version (3.3.3-RC10) available for the following hardware devices :
CoreLP / CoreHP:
  32-bit platform: base-installer_x86_slave*.sqfs
  64-bit platform: masep-core-core-3.3*.mender
D9S2-A screen (Display9):
  32-bit platform: ccpilot_i386-2.25.x/2.26.x, or
  64-bit platform: masep-display-x900-3.3.x
D9S2-B screen (X900):
  Can only runs 64-bit platform: masep-display-x900-3.3*.mender
Reference:
https://confluence.hexagonmining.com/display/TR/MASEP+TRM+-+Overview+of+MASEP
https://confluence.hexagonmining.com/display/9HSDR/9106+Display+Replacement+Hexagon+Naming
Notes: On June 30th, 2023, MASEP 3.3.18 version

## Slide 15: MineOperate OP Pro Software
MineOperate OP Pro 2.8-005 is released particularly to support running Ruby Panel on 64-bit platform MASEP screen, with Core box still runs on 32-bit platform.
OP Pro 2.8-005
File | Description
app-jspanel-all-2.8-005-b383.05e8ac3431071c9a790fea11fd4c18c8b773d285.sqfs | JSPanel – installed on Screen
app-oppro-x86-2.8-005-b383.05e8ac3431071c9a790fea11fd4c18c8b773d285.sqfs | JAMS – installed on Core
app-ruby-gtk2-imx8-2.0-1.sqfs | 64-bit Ruby for imx8 screen (D10S5-A/V1000)
app-ruby-gtk2-x86_64-2.0-1.sqfs | 64-bit Ruby for Intel x86_64 architecture screen (D9S2-B/X900)
install | Install script for OTA update
Mirror | URL
Brisbane | http://abri-hydra.lgs-net.com:81/Releases/2.8/Products/005/
Tucson | https://hexagonna.jfrog.io/ui/repos/tree/General/OpPro/Releases/2.8/Products/005
Artifact's locations for equipment running MASEP: http://abri-hydra.lgs-net.com:81/Releases/2.8/Products/005/common-x86/2.8-005/
Existing equipment that runs on 32-bit hardware still uses the application architecture as before, with the relevant tar.gz artifacts under http://abri-hydra.lgs-net.com:81/Releases/2.8/Products/005/, ie: uhp-mojo, uhp-arm, winsys, etc.

## Slide 16: MineOperate OP Pro Software
Panel Variants | Minimum Platform Release | Supported OP Pro Release
LP Equipment Panel (Ruby Panel): - LP Truck, LP Shovel, LP Grader | 3.3.3 | 2.8-005
LP Equipment Panel (Chromium Web Panel): - LP Truck, LP Shovel | 3.3.3 | 3.1-001
What already tested:

## Slide 17: MineOperate OP Pro Software
Panel Variants | Minimum Platform Release | Supported OP Pro Release
LP Equipment Panel (Ruby Panel): - LP Drill, LP Dozer, LP Loader, LP Water Truck, LP Fuel Truck, LP Explosive Truck HP Equipment Panel (Ruby Panel): - HP Drill, HP Shovel (without NAV Tab/NAFTA Version) | 3.3.3 | 2.8-005
HP Equipment Panel with NAV Tab enabled (Ruby Panel APAC Version): HP Shovel, HP Dozer, HP Loader | 3.3.3 | 2.8-005.x (Scheduled priority in next PI)
LP Equipment Panel (Onboard Shell App): LP Truck, LP Shovel | 3.3.3 | 3.1-001
What not yet tested:

## Slide 18: Platform Installation
Migrating Screen to MASEP Image
Performed when preparing the screen for production or repair (i.e: workshop)
Download Platform Image for Production: https://hexagonna.jfrog.io/artifactory/masep-artifacts/Releases/3.3.x/images-for-production
Preparing USB Key and Installation Procedure: MASEP TRM - Migrating a Display9/X900 to 64bit MASEP
  Plug the USB key for OS migration
  Reboot/Power up the Screen
  Press F11 to enter boot selection menu, choose boot from USB key
  Select kernel options and boot kernel menu, choose “Graphic console install”
  Image installation confirmation, type 'y' on keyboard
  Image copy started
  Image copy completed
  Remove USB key and press Enter to reboot
  Screen powering up
  System Menu

## Slide 19: Software Installation: OP Pro 2.8-005
USB Key Install
Performed at site to flash/program the appropriate equipment to run Ruby Panel
Platform Files:
Mender Image (masep-display-x900-3.3*.mender) for field use: https://hexagonna.jfrog.io/ui/native/masep-artifacts/Releases/3.3.x/images-for-field-use
32-bit Core (base-installer_x86_slave_2.26.5*.sqfs): https://hexagonna.jfrog.io/ui/native/embedded_artifacts/yocto_artifacts/releases/2.26.5/common-x86/installer
Application Components:
D9S2-B screen (X900) - MASEP 64-bit:
  64-bit Ruby - app-ruby-gtk2-x86_64-2.0-1.sqfs
  JSPanel - app-jspanel-all-2.8-005-b383.05e8ac3431071c9a790fea11fd4c18c8b773d285.sqfs
CoreLP /CoreHP - ccpilot 32-bit:
  PlatformService - app-platform-services-core_i386 extracted from usbkey-ccpilot_i386_2.26.5-88f0d98a-b5.zip
  JAMS - app-oppro-x86-2.8-005-b383.05e8ac3431071c9a790fea11fd4c18c8b773d285.sqfs

## Slide 20: Software Installation: OP Pro 2.8-005
USB Key Structure MASEP 3.3.3 rc13 or older
/
├── apps/
│ ├── app-oppro-x86-2.8-005-*.sqfs
│ └── app-platform-services-core_i386_*.sqfs
├── apps-allarch/
│ ├── app-ruby-gtk2-x86_64-1.9-1.sqfs
│ └── app-jspanel-all-2.8-005-*.sqfs
├── base-installer_x86_slave_*.sqfs
├── hmcmd_config/
│ └── <equipment>-hmcmd.conf
├── masep-display-x900-*.mender
└── setup.sqfs
Reference
https://confluence.hexagonmining.com/display/PPC/%5BWiP%5D+Running+OP-Pro+v2.8+ruby+panels+on+MASEP+screen+with+32bit+Corebox

## Slide 21: Software Installation: OP Pro 2.8-005
USB Key Structure MASEP 3.3.3 rc15 or newer
Reference
https://confluence.hexagonmining.com/pages/viewpage.action?pageId=281891574

## Slide 22: Software Installation: 2.8-005
Preparing hmcmd.conf file (global configs)
"version": "1.1",
"machine": "EXAMPLE-X900",
"ip_address": "10.5.0.205",
"timezone": "America/Sao_Paulo",
"appserver": "192.168.0.13",
"ntpserver": "192.168.0.13",
"vpnserver": "192.168.0.13",
"vpn_protocol": "udp",
"vpn_port": "1194",
"vpn_network": "10.40.0.0",
"vpn_netmask": "255.255.255.0",
"sl_gateway": "192.168.200.45",
"legacy_openvpn_nopull": "false",
"mqtt_broker": "localhost",
Parameter | Description
version | Hmcmd version, in this case, it's always 1.1
machine | Equipment name to be configured. Make sure this name matches the filename <machine>-hmcmd.conf
ip_address | ip address registered in OP Pro devices
timezone | timezone to be configured in both screen and core box
appserver | Jigsaw server IP (will be used to create jamssql host)
app_manager_server | IP address of the 'App Manager' server that maintains the list of applications (and HW config) for this equipment. – when site is using Asset Health, this will be referring to Asset Health server address in which the equipment can connect to
ntpserver | NTP server
vpnserver | IP address of the computer running the OpenVPN server, usually a Jigsaw Server.
vpn_protocol | Protocol of VPN connection as configured in the server
vpn_port | Port in which the server is running the VPN
vpn_netmask | Subnet of the OpenVPN network
sl_gateway | Always set to 192.168.200.45
legacy_openvpn_nopull | New installer automatically adds ‘route-nopull’ on openvpn configuration, which applicable if customer does not want to reach a server or network behind OpenVPN (JAMS) server. But if Core box need to be able to reach Asset Health server (behind Jigsaw openvpn server), the route-nopull must not be created to allow additional static route on core box (set to false)
mqtt_broker | If set to localhost, openvpn client will run on Corebox. If set to master, openvpn client will run on screen. Always set to ‘localhost’
Reference: https://confluence.hexagonmining.com/display/~NUAR/Hmcmd+v1.1+Global+Parameters
*) bold: keep entries as is

## Slide 23: Software Installation: 2.8-005
Preparing hmcmd.conf file (components)
"components": [
{
"role": "wifi_router",
"hwtype": "Core",
"interface": "wlan1",
"wl_ipaddr": "192.168.0.205",
"wl_netmask": "255.255.255.0",
"wl_gateway": "192.168.0.1",
"wl_essid": "ssid",
"wl_encrypt": "psk",
"wl_key": "passwd"
},
{
"role": "lp_position_provider",
"hwtype": "Core"
}
],
Parameter | Description
role | wifi_router – required if the equipment is meant to use WiFi to communicate with a server. mobile_router – required if the equipment is meant to use 4G/LTE comms to a server. lp_position_provider - required for equipment using low-precision GNSS (CoreLP) – default position_period is 1s hp_position_provider - required for equipment using high-precision GNSS (CoreHP) – default position_period is 0.1s
hwtype | Core
interface | The name of wireless lan (wlan0 to wlanX depending on the hardware). In Core, wlan0: wifi with single antenna, wlan1: wifi with dual antenna
wl_ipaddr | The IP address to use on the wifi interface Can also be set to dhcp.
wl_netmask | The netmask to use on the wifi interface.
wl_gateway | The gateway to use on the wifi interface.
wl_essid | The SSID to connect to.
wl_encrypt | The shared key to use with psk and psk2.e, psk, psk2, wep.
wl_key | Protocol of VPN connection as configured in the server
https://confluence.hexagonmining.com/display/PPC/wifi_router
https://confluence.hexagonmining.com/display/PPC/mobile_router
https://confluence.hexagonmining.com/display/PPC/lp_position_provider
https://confluence.hexagonmining.com/display/PPC/hp_position_provider
*) bold: keep entries as is

## Slide 24: Software Installation: 2.8-005
Preparing hmcmd.conf file (applications)
"applications": [
{
"app": "platform-services-core",
"device": "slave",
"enabled": "true",
"filename": "app-platform-services-core_*.sqfs"
},
{
"app": "app-oppro-on-core",
"device": "slave",
"enabled": "true",
"filename": "app-oppro-x86-*.sqfs"
},
{
"app": "jspanel-on-display",
"device": "master",
"enabled": "true",
"filename": "app-jspanel-*.sqfs",
"hosts": {
"sqlhost":"192.168.200.45"
}
},
{
"app": "ruby-gtk-on-display",
"device": "master",
"enabled": "true",
"filename": "app-ruby-gtk2-x86_64*.sqfs"
},
],
*) bold: keep entries as is
Reference:
MASEP API - Custom Hosts Entries

## Slide 25: Software Installation: OP Pro 2.8-005
USB Installation Step
Reference
Sample Setup Preparation and Recording: https://confluence.hexagonmining.com/pages/viewpage.action?pageId=281891574
Installation Sequence | Notes
Plug the USB key for equipment flashing | 
System Menu: Loading Equipment Selection Screen | 
System Menu: Select an Equipment and load its information | Select equipment from the list, and then confirm
Setting up Installation | 
Installation Progress: DISPLAY_9 Prepare | 
Installation Progress: DISPLAY_9 OS Update | Screen rebooted
Installation Progress: DISPLAY_9 Apps Update | 
Installation Progress: DISPLAY_9 Reconfigure | Screen rebooted
BaseCore OS Update | Core rebooted
BaseCore Apps Update | 
BaseCore Reconfigure | 
OP Pro Ruby JSPanel loading.. | 

## Slide 26: MineOperate OP Pro Software
MineOperate OP Pro 3.1-001 (Chromium Web Panel) support 64-bit MASEP Screen, with Core box running 32-bit platform:
OP Pro 3.1-001
File | Description
app-oas-x86-6.2-22-b416.f0e95f96ca9361cbeb09d16a8cb29a78adb86dc1.sqfs | GVOS package – installed on Core
app-oppro-x86-2.8-005-b383.05e8ac3431071c9a790fea11fd4c18c8b773d285.sqfs | JAMS package – installed on Core
install | Install script for OTA update
app-webpanels_common-x86_1.0.5-b180.de1dc542daac030ef13a5bf7b756d0126ed91ac4.sqfs | Webpanels – installed on Core
app-oppro-MASEP_all-v4.sqfs | MASEP OPPro webpanel startup script for Screen
Mirror | URL
Brisbane | Index of /Releases/3.1/Products/001 (lgs-net.com)
Artifact's locations for equipment:
Index of /Releases/3.1/Products/001/corelp-x86/sqfs_display (lgs-net.com)
https://hexagonna.jfrog.io/ui/native/embedded_artifacts/app.sqfs%20on%20MASEP

## Slide 27: Software Installation: OP Pro 3.1-001
USB Key Install
Performed at site to flash/program the appropriate equipment to run Chromium Web Panel
Platform Files:
Mender Image (masep-display-x900-3.3*.mender) for field use: https://hexagonna.jfrog.io/ui/native/masep-artifacts/Releases/3.3.x/images-for-field-use
32-bit Core (base-installer_x86_slave_2.26.5*.sqfs): https://hexagonna.jfrog.io/ui/native/embedded_artifacts/yocto_artifacts/releases/2.26.5/common-x86/installer
Application Components:
D9S2-B screen (X900) - MASEP 64-bit:
  OP Pro MASEP - app-oppro-MASEP_all_v4.sqfs
CoreLP /CoreHP - ccpilot 32-bit:
  PlatformService - app-platform-services-core_i386 extracted from usbkey-ccpilot_i386_2.26.5-88f0d98a-b5.zip
  JAMS - app-oppro-x86-3.1-001-b299.a7e4910fdc2b019d8fc00d031b1bd58a20111636.sqfs
  GVOS - app-oas-x86-6.2-22-b416.f0e95f96ca9361cbeb09d16a8cb29a78adb86dc1.sqfs
  Webpanel - app-webpanels_common-x86_1.0.9-b194

## Slide 28: Software Installation: 3.1-001
USB Key Structure
/
├── apps/
│ ├── app-oppro-x86-3.1-000_013-b339*.sqfs
│ ├── app-oas-x86-6.2-22*.sqfs
│ ├── app-platform-services-core_i386_*.sqfs
│ └── app-webpanels_common-x86*.sqfs
├── apps-allarch/
│ └── app-oppro-MASEP_all_v4.sqfs
├── base-installer_x86_slave_2.26.5-r1360.sqfs
├── hmcmd_config/
│ └── <equipment>-hmcmd.conf
├── masep-display-x900-*.mender
└── setup.sqfs
Reference
https://confluence.hexagonmining.com/display/PPC/Running+OP-Pro+v3.0+web+panels+on+MASEP+screen+with+32bit+Core+box

## Slide 29: Software Installation: 3.1-001
Preparing hmcmd.conf file (applications)
"applications": [
{
"app": "platform-services-core",
"device": "slave",
"enabled": "true",
"filename": "app-platform-services-core_*.sqfs"
},
{
"app": "jams-on-core",
"device": "slave",
"enabled": "true",
"filename": "app-oppro-x86*.sqfs"
},
{
"app": "gvos-on-core",
"device": "slave",
"enabled": "true",
"filename": "app-oas-x86-*.sqfs"
},
{
"app": "webpanels-core",
"enabled": "true",
"device": "slave",
"filename": "app-webpanels*.sqfs"
},
{
"app": "oppro-display-MASEP",
"enabled": "true",
"device": "master",
"filename": "app-oppro-MASEP*.sqfs"
}
],
For “global configs” and “components” section, the reference is similar with 2.8-005
*) bold: keep entries as is

## Slide 30: Software Installation: OP Pro 3.1-001
USB Installation Step
Reference
Sample Setup Preparation and Recording: https://confluence.hexagonmining.com/pages/viewpage.action?pageId=281890534
Installation Sequence | Notes
Plug the USB key for equipment flashing | 
System Menu: Loading Equipment Selection Screen | 
System Menu: Select an Equipment and load its information | Select equipment from the list, and then confirm
Setting up Installation | 
Installation Progress: DISPLAY_9 Prepare | 
Installation Progress: DISPLAY_9 OS Update | Screen rebooted
Installation Progress: DISPLAY_9 Apps Update | 
Installation Progress: DISPLAY_9 Reconfigure | Screen rebooted
BaseCore OS Update | Core rebooted
BaseCore Apps Update | 
BaseCore Reconfigure | 
Web Panel: Connecting to the HTTP server, application server, Loading the database schema, model data .. | 

## Slide 31: Application OTA Update
Ruby Panel on MASEP Screen
Link: Over The Air - OTA. How to install on OP Pro 2.8-005.
The OTA update relies on /opt/Jigsaw/Services/jams-owrt-update script in Core box. This is only suitable for updating app-*.sqfs file (not platform files).
File structure to be prepared on server, example:
    /opt/Jigsaw/Releases/common-x86
    └── 2.8-005.001
    └── sqfs
    ├── app-jspanel-all-2.8-005_*.sqfs
    ├── app-oppro-x86-2.8-005_*.sqfs
    └── install
Procedure (refer to MOPS-26156):
Download sqfs and install files from http://abri-hydra.lgs-net.com:81/Releases/2.8/Products/005/common-x86/2.8-005/
Create new <version> folder under /opt/Jigsaw/Releases/common-x86/
Create sqfs folder inside the new <version> folder
Copy the files: app-jspanel*.sqfs, app-oppro-*.sqfs, install
Update ‘sofware_version’ of given equipment in OP Pro Manager Device view to the new version.
Log file:
Server (unchanged): /var/log/rsyncd.log
Onboard (Core box): /opt/Jigsaw/Logs/jams.install.log

## Slide 32: Application OTA Update
Web Panel on MASEP Screen
Link: Over The Air - OTA. How to install on OP Pro 3.0-002-012 and 3.1.
The OTA update relies on /sbin/owrt-update script in Core box. . This is only suitable for updating app-*.sqfs file (not platform files).
File structure to be prepared on server:
    /opt/Jigsaw/Releases/corelp-x86
    └── 3.1-001
    └── sqfs_core
    ├── app-oas-x86-6.2-22*.sqfs
    ├── app-oppro-x86-3.1-001-*.sqfs
    └── install
Procedure:
Download sqfs and install files from http://abri-hydra.lgs-net.com:81/Releases/3.0/Products/003/webpanels/OTA/sqfs/
Create new <version> folder under /opt/Jigsaw/Releases/corelp-x86/
Create sqfs folder inside the new <version> folder
Copy the files: app-oas*.sqfs, app-oppro-*.sqfs, install
Update ‘sofware_version’ of given equipment in OP Pro Manager Device view to the new version.
Log file:
Server (unchanged): /var/log/rsyncd.log
Onboard (Core box): /opt/Jigsaw/Logs/jams.install.log

## Slide 33: Platform Remote Update
Mender file update
The update is only applicable for .mender file (not app*sqfs, base-installer, etc) and done manually for each equipment.
The .mender file can be a full mender image (i.e: 3.3.3-RC10 masep-display-x900-3.3.3-r96fbd074-b245.mender)
But can also delta image, which is smaller, but the file must be relevant to the current build version on the equipment, i.e: from RC8  RC10 (masep-display-x900-3.3.3-rfd435d5c-b235-delta-3.3.3-r96fbd074-b245.mender)
Relevant mender file (full and certain delta image) is available on Platform Release page (i.e: Platform Release 3.3.3)
Procedure to update MASEP Screen:
Copy mender file from OP Pro server to equipment's screen, i.e:
  rsync -avz -e 'ssh -p 2022' --progress masep-display-v1x00-3.3.3-rf9459659-b51.mender hexagon@<equipment_name>:/tmp/.
ssh to screen, execute ‘mender install’ command
  sudo mender install masep-display-v1x00-3.3.3-rf9459659-b51.mender
Reboot screen
ssh to screen, execute ‘mender commit’ command
  sudo mender commit
Reference:
MASEP Testing: Remote upgrade mender image file (Screen)
MASEP - Platform Software (Image) Updates

## Slide 34: Appendix
Quick Notes
MASEP Screen:
  Primary display being used is virtual desktop #7 (Ctrl+Alt+F7), the other desktop can be used for terminal session (i.e: Ctrl+Alt+F1 ..Fn)
  To ssh from Core box to Screen:
    ssh hexagon@master
  To ssh from OP Pro server directly to screen, we can use port 2022:
    ssh –p 2022 hexagon@<equipment-name>
  ssh user/password (hexagon user will cover everything needed):
    hexagon/m4s3p
    root/suseroot
  JSPanel process is called from mining-gui service:
    check status: sudo systemctl status mining-gui|cat
    stop: sudo systemctl stop mining-gui
    start: sudo systemctl start mining-gui
    restart: sudo systemctl restart mining-gui

## Slide 35: Appendix
Quick Notes
MASEP Screen:
  Check platform version:
    mender: sudo mender show-artifact
    platform build: grep BUILDNO /etc/board-arch
  JSPanel log file:
    /opt/Jigsaw/Logs/jspanel.log
  System log file:
    /var/log/messages
  Platform installation log file:
    /opt/install.log
  Command/Log files of interest in case of operating system related problem:
    /var/log/weston.log
    dmesg –T
    sudo systemctl status | cat

## Slide 36: Appendix
Quick Notes
Core:
  To ssh from Screen to Core box:
    ssh jigsaw@sensorbox
  ssh from OP Pro server to equipment will bring you to Core box:
    ssh <equipment-name>
  ssh user/password is jigsaw/jigsaw
  JAMS process is called from /etc/init.d/jams:
    stop: sudo /etc/init.d/jams stop
    start: sudo /etc/init.d/jams start
    restart: sudo /etc/init.d/jams restart
JAMS onboard sqlite db file:
  /tmp/jmineops.db
To run query on sqlite db:
  sqlite3 /tmp/jmineops.db

## Slide 37: Appendix
Quick Notes
Core:
  JAMS log file:
    /opt/Jigsaw/Logs/jams.log
  System log file (including openpvn):
    /opt/Jigsaw/Logs/messages*
  Command of interest in case of operating system related problem:
    dmesg

## Slide 38: Appendix
Installation Gotchas
Problem Description | To Check
After plugging in the USB key, there is nothing happen | Check if the appropriate files and folder has been created correctly on the USB key. When the USB key was used earlier for low-level format (BOOT/load hddimg), you will need to clean/remove all partition (not only format with FAT32 default allocation size) prior to use it for equipment flashing
After plugging in the USB key, there are no equipment selection shown. But there is a terminal window popping up showing usb_monitor log and updating mender file. | When a .mender file is exist but there are no 'hmcmd_config' directory, the system will automatically execute mender update: Check if hmcmd_config directory exist and correct (no typo) Check if the proper <equipment>-hmcmd.conf already created inside the hmcmd_config directory Double-check the content of <equipment>-hmcmd.conf. Compare against sample entries for hmcmd.conf file from the appropriate MASEP Release: https://confluence.hexagonmining.com/display/PPC/%5BWiP%5D+Running+OP-Pro+v2.8+ruby+panels+on+MASEP+screen+with+32bit+Corebox
During the installation, there are error messages generated "no app-*.sqfs found" | Make sure the appropriate sqfs file is exist on relevant folder. Check inside the relevant <equipment>-hmcmd.conf file: Ensure the json structure file is correct and there are no typo (i.e: use Json Viewer plugin for Notepad++) Ensure the entry for the 'filename' in 'application' section is relevant with the actual sqfs file name. When the USB key was removed incidently in the middle of Installation and then re-plug, the path to some files/directory may have been changed and failed to get recognized. In this case, after the failure installation finished, one would need to re-start the installation from beginning (i.e: re-plug USB key, selecting the equipment, etc) For above case, there's also possibility of bad USB Flashdrive / Dongle hardware.

## Slide 39: Appendix
Installation Gotchas
Problem Description | To Check
Installation completed, but the screen just stay on Jigsaw Splash screen forever: central JAMS is not accessible | Screen Check if screen able to talk with Corebox ping sensorbox 2. Check if screen able to talk with Jigsaw server ping jamshost 3. Check if screen able to talk with sqlhost (using core box address: 192.168.200.45) ping sqlhost Core 1. When using wifi, check if the wifi is setup correctly and able to connect to server address sudo ifconfig wifi sudo iwconfig ping vpnhost When using LTE, check if mobile modem is setup correctly and able to connect to server address sudo ifconfig wwan0 sudo wan info ping vpnhost 2. Check if the openvpn tunnel is up and able to connect, or there any error sudo ifconfig tun0 grep openvpn /var/log/messages ¦ tail -30 3. Check if jams onboard able to communicate with server, or there any error: tail -F /opt/Jigsaw/Logs/jams.log 4. Check if JAMS on server is running and accessible from equipment telnet jamshost 1110

## Slide 40: Appendix
Installation Gotchas
Problem Description | To Check
Installation Process not completed with message "Installation failed' | Check if the appropriate files and folder has been created correctly on the USB key:USB File Structure when using MASEP >= v3.3.1 The error message may also be the consequence of app-sqfs that not getting installed properly on previous attempt, refer to section where error messages generated "no app-*.sqfs found for things to check.
When doing some changes on hmcmd.conf file, the changes are not being read after inserting USB key and still uses the old one somehow | Remove the site-ConvertedHmcmdConfig.sqfs that was created from previous installation in the USB key. It will get re-created next time you plug the USB
Previous equipment installation not succeeded (because of bad file, etc) and we want to start over | #1: As an attempt to clear out any previous installation cache on Screen: Make sure install USB key is unplugged from screen sudo systemctl stop masep-manager system-menu sudo rm -rf /var/lib/masep-manager sudo systemctl start masep-manager system-menu Plug the USB key to start installation again #2: If the above failed, to clean previous configuration on Core and Screen: Core: Plug the USB Key contain base-installer*.sqfs file directly to USB Core box using USB dongle. Wait for the led indicator in Core box to blink really fast, and then remove the USB This will leave the Core in “unconfigured” state Screen: This command will remove any custom changes, like configurations, hostnames, application installed, ssh fingerprint, etc: sudo rm -rf /data/overlay/*/*/; sudo reboot For last resort, perform the MASEP migration steps (using hddimg file loaded into bootable usb) to reset the screen

## Slide 41: Appendix
Known Limitation
Description | Note
VNC not available | For ruby panel (2.8-005), there are steps provided in PLAT-4649 to enable the screen-share in configuration files, but with some caveats: Remote performance is poor even with good comms (3~5 sec delay) Mouse pointer from old remote session is drawn in panel This is not final and remote screen options is still being investigate.
OreNAV not available | MOPS-26275 2.8-005: OreNav QA - X900

## Slide 42: What’s Next
OP Pro version on Customer needs to be upgrade to version 2.8-005
There is no database change between 2.8-003 and 2.8-005, so the version would be compatible. For initial stage to not block the deployment of new screen would not be a problem when server is not upgraded. But we should be planning to upgrade the server in the next steps yet.
Raise IN ticket request for PD to create 2.8-005 site branch for each of relevant Customer

## Slide 43
Thank you.
Notes: Thank you.