## Slide 1
Program
MineOperate Technical Level 2
Optimizer
Edgar Sepulveda
Global Technical Manager, MineOperate
Date: 07/31/2023
Version: OP Pro 3.1-001

## Slide 2: Optimizer
Outline
Introduction
  What is optimization?
  Overview of Optimizer
The Linear Programming Layer
  Description
  Structure
  Solution procedure
The Dynamic Assignment Layer
  Shovel Assignments
  Dump Assignments
  Reassignments
  Fuel Assignments
  THPH Assignments

## Slide 3: Optimizer
What is optimization?
To make the best or most effective use of (a situation or resource).
Notes: Optimization is used in every industry

## Slide 4: Optimizer
Optimization Example
Barley
12 acres
$120/tonne
Corn
15 acres
$84/tonne
Wheat
11 acres
$23/tonne
Chart: 
| 0.7 | 1.8 | 2.6 | 5
Yield | 2.7 | 3.2 | 3.5 | 3.6
Chart: 
| 0.7 | 1.8 | 2.6 | 5
Yield | 8 | 8.5 | 8.6 | 9
3 fields of different crops (3 different prices).
Each crop responds differently to fertilizer (different yields).
How should the farmer distribute his fertilizer to maximise his $?
Chart: 
| 0.7 | 1.8 | 2.6 | 5
Yield | 0.1 | 2.2 | 4 | 6
Notes: A farmer has $10,000 to spend on fertilizer
He has 3 fields of different crops
Each crop will respond differently to fertilizer (different yields)
Each crop has a different selling price
Where should he put his fertilizer to maximise his total revenue?
Optimize (make best use of) the fertilizer to maximise total revenue

## Slide 5: Optimizer
What does ‘the best use of’ mean in mining?
The definition of ‘the best use of equipment’ varies from mine to mine and indeed at any given mine from day to day. Optimizer is extremely flexible and configurable for this reason, however some of its common goals include:
Minimizing non-productive equipment time (e.g., truck queuing, shovel idle).
Achieving the maximum amount of material movement.
Delivering a specified amount of certain materials to meet a blending requirement.
Minimizing the impact of planned operator breaks.
Managing truck tire duties.

## Slide 6: Optimizer
FMS – Not Optimized
  The number of combinations and permutations of dispatching trucks to shovels, dumps and crushers grows exponentially with the number of nodes (shovels and dumps).
  Many inputs required for optimal decisions (Fuel, TKPH, shift change, blending, etc.).
  Human dispatching can not make optimal decisions.
  Terrain is constantly changing which affects decision making.

## Slide 7: Optimizer
The Main Task of Optimizer
The main task of Optimizer is to maximize the production of the mine by computing truck assignments.

## Slide 8: Optimizer
Optimizer Principles
  Real-time problem solver, utilising complex mathematical algorithms to compute sets of optimal path rates between shovels and dumps.
  The primary goal is to reduce truck queue and shovel hang times, thereby increasing productivity.
Notes: The Jigsaw Jmineops system contains state of the art optimisation algorithms which use the processing power and the network bandwidth of modern computer systems to provide optimised truck allocation. This is called Joptimiser.
This Joptimiser is designed to intelligently control fleet and material movements across the entire mining operations.
By using the innovative distributed SQL (structured query language) database architecture of Jmineops, these algorithms achieve precise truck tracking, arrival time prediction and idle time prediction which are not possible with RPC message based systems of the past. The Jmineops algorithms combine many techniques used and proven in the past systems with new algorithms made possible by the use of modern PC based components in a distributed, high speed wireless LAN. By combining modern powerful PC hardware with distributed database architecture, Jmineops achieves a level of scalability and optimisation not possible with legacy architectures.
Joptimiser functions are:
Optimal solutions are published by the central server and implemented by the truck modules in the filed
ETAs and queue information is used to generate assignments to shovels
Truck modules can make assignments decisions in case the network or the system are down
Historical dug rates are maintained for each shovel to avoid under or over feeding

## Slide 9: Optimizer
Optimizer Components
Optimizer relies on a set of complex mathematical algorithms to solve real-time production optimization problems. These are:
Linear Programming (LP) layer
Dynamic Assignment (DA) layer
Notes: Jigsaw as a real-time problem solver relies on the components in the Joptimiser to effect assignments.
There are two components to Joptimizer:
Linear Programming (LP) layer
Dynamic Assignment (DA) layer, both based on a set of complex mathematical algorithms.
Jmineops the computer models mentioned in the Joptimiser above to optimisation server recomputes the future shovel assignments with expected time of arrival (ETAs) for all trucks when any truck loads at a shovel or dumps at a dump. This ensures that the next optimal shovel assignment is always available in the replicated assignment record onboard each truck and eliminates communications problems at dumps which may temporarily have minimal or nil radio coverage.
LP Layer
The LP layer is the theoretical master plan for maximizing overall production in the mine. This layer contains optimal shovel and dump circuits that indicate:
Which shovels should provide loaded trucks to dumps and the number of trucks require to cover the shovels.
Which dumping locations should provide empty trucks to which shovels and the number of trucks required to cover the shovels.
The Linear programming views shovel to dump circuits as flow rates or “imagines” it as a conveyor belts or pipelines connecting the loading and dumping points and that material is continuously and evenly moving between them.
DA Layer
The DA layer tries to achieve the flow rates outlined in the LP with real-time truck assignments. As the Jigsaw system receives truck assignment requests from the field the DA attempts to enforce that in the LP by assigning empty trucks to feed the shovel/dump flow rates.

## Slide 10: Optimizer
Optimizer Components

## Slide 11: Linear Programming Layer
LP Layer Agenda
What is linear programing?
Objective function
Input variables
Constraints
Solution procedure
LP recalculation

## Slide 12: Linear Programming Layer
What is Linear Programming?
Linear programming (LP) is a method to achieve the best outcome (such as maximum profit or lowest cost) in a mathematical model whose requirements are represented by linear relationships.
Linear programming is a special case of mathematical programming.
Linear programming models are defined:
  Objective function.
  Input Variables.
  Constraints.

## Slide 13: Linear Programming Layer
Optimizer Objective Function
The Optimizer objective function represents the hauling requirements necessary to cover dig rates in every feasible hauling route.
The resulting LP solution represents the rate at which the system should assign trucks to each haulage path.
By minimizing this function, Optimizer maximizes the production achievable with the current trucks and shovels.

## Slide 14: Linear Programming Layer
Optimizer Input Variables
If we think of the structure of a mine, we could describe it as a series of locations/nodes that are interconnected by pathways or routes.
Excavation points are load nodes and tipping points are dump nodes; and trucks travel between load nodes and dump nodes.
The Optimizer input variables are the nodes and the routes between nodes.

## Slide 15: Linear Programming Layer
Optimizer Constraints
Continuity
Material
Digging Rates
Blending
Available Truck Haulage
Shovel Restrictions
Grade Restrictions
Material Priorities
Shovel Coverage Factors

## Slide 16: Linear Programming Layer
Continuity constraints
The total flow into a shovel or dump must equal the flow out of that shovel or dump.

## Slide 17: Linear Programming Layer
Material Constraints
(High level) material constraints force shovels digging waste to feed waste dumps and shovels digging ore to feed appropriate crushers, stockpiles, or leach dumps.
A dumping location accepts one or more of the enumerated material types. When a shovel specifies the grade(s) being dug, the Optimizer configures paths only to those dumps which accept the material being dug by the shovel.

## Slide 18: Linear Programming Layer
Shovel Digging Rates
Each operating shovel has a limit on the rate at which it can produce material.
The on-board JAMS system continuously measures and updates this digging rate by measuring the time required to spot and load each truck and the tonnage of material produced.
Optimizer incorporates this digging rate as a constraint which specifies that the total of all paths leaving a shovel must be less or equal to the shovel's maximum dig rate.

## Slide 19: Linear Programming Layer
Blending Constraints
Optimizer enforces blending constraints to control the quality of material produced at specific dumps. To configure blending, the mine specifies a list of material qualities for each material block.
For example, a gold/copper mine might specify %Au and %Cu as material qualities. Each material block contains assayed values for all the quality parameters, typically obtained from the mine planning system.
Optimizer uses the Blend Model table to define different blending constraints that comprise constraints in the LP simplex model (see Blending Module).

## Slide 20: Linear Programming Layer
Available Truck Haulage Constraints
Mines often operate with less trucks than are required to completely cover the shovels. In these under-trucked scenarios, Optimizer optionally adds a total truck haulage constraint which automatically decreases feed rates to low priority or long-haul shovels such that the required truck haulage matches that actual available truck haulage (see Match Trucks).
For mines which incorporate multiple pits, Optimizer creates separate haulage constraints for each pit to avoid starving shovels in one pit due to insufficient trucks in another pit.

## Slide 21: Linear Programming Layer
Shovel Restrictions
Optimizer supports locking of shovels to specific dumps or restricting shovels from feeding certain dumps.
These constraints are more restrictive than material constraints, since they force Optimizer to only consider specific dumps as candidates for assignments.

## Slide 22: Linear Programming Layer
Grade Restrictions
Optimizer supports locking of grade blocks to dumps or restricting a specific grade block from being assigned to certain dumps. These restrictions are less restrictive than shovel restrictions since they only apply to shovels digging a specific material block.

## Slide 23: Linear Programming Layer
Shovel Priorities
Optimizer supports low, medium, and high priorities for any shovels. Shovel priorities ensure that high priority shovels are covered preferentially over lower priority shovels.

## Slide 24: Linear Programming Layer
Material Priorities
Optimizer supports low, medium, and high priorities for all material types defined in the enumeration database.
Unlike shovel priorities, material priorities only apply to shovels when that shovel is digging the selected material type. If a shovel changes from digging ore to waste, it automatically switches to the associated waste priority.

## Slide 25: Linear Programming Layer
Shovel Coverage Factors
Optimizer supports a percent coverage factor for each shovel. Setting the coverage factor less than 100% allows the mine to cover high priority shovels up to the specified percentage, with the remaining coverage being distributed among lower priority shovels.
Coverage factors can also be higher than 100% to insure minimal hang time for very high priority shovels.

## Slide 26: Linear Programming Layer
LP Solution Procedure
Create node properties
Set size of truck
Check Match Trucks
Create feasible routes
Create restrictions
Create LP nodes
Initialize array of constraints
Create continuity constraints for dump nodes
Create capacity constraints for load nodes
Create continuity constraints for load nodes
Create capacity constraints for dump nodes
Create current haulage
Create objective function
Assign haulage rates to routes

## Slide 27: Linear Programming Layer
LP Solution Procedure – Node Properties
Name: (name), name of the shovel or Dump location.
Node type: (nodeType), the node class, may be LPNODE_SHOVEL for shovels, or for dumps LPNODE_CRUSHER, for crushers or LPNODE_STOCKPILE, for Stockpiles or LPNODE_DUMP for dumps.
Feed rate: (feedRate), flow rate goal in tons per hour.
Capacity: (capacity), capacity or maximum feed rate, in tons per hour.
SpotTime: expected Spotting time, given in seconds.
Percentage of coverage: (percentCoverage), percentage of coverage desired, in percentage.
Materials: (materials), list of materials produced by the load node, or accepted by the dump node.
Polygons: (grades), list of polygons produced by the node of load.
State: (status), the node of load or dump node.
Region: (region), a Region where the node of load is located or Dump.
Material: (material), last material produced by the node of load.
Location: (location), location of load node or the Dump node.
A: fixed (lockedTo), Dump node to which this load node is locked.
ID shovel: (shovel), id related to the node of load in question.
Priority of shovel: (priority), priority configured for the load node.
Notes: This step of the solution procedure analyzes all existing nodes in the system. As we have already seen, a node can be a loading location or a dump location and each node has certain associated properties that are used in various parts of the solution procedure.
This list of properties contains not only requirements (e.g. feed rate) but also configurable parameters such as the shovel priority and the coverage percentage. In addition to this it contains variables that represent the current conditions of that node such as State, location, polygons, etc.
We can immediately see that some of these parameters may influence the LP solution, later we will see in detail how such requirements affect the Joptimizer’s result.

## Slide 28: Linear Programming Layer
LP Solution Procedure – truck size
Finds the set value of the standard truck in the system.
Notes: This part of the process is quite simple, since it simply finds the set value of the standard truck in the system. This value is recommended to be the average of the capacity of all trucks configured in the system.

## Slide 29: Linear Programming Layer
LP Solution Procedure – Match Trucks
Checks if Match Trucks is selected.
If it is, Optimizer will favour the short routes within the mine.
Notes: For example, if you have 1 truck and 2 shovels; and one shovel has a haul distance of 2 Km and the other has a distance of 10 km, to maximize production (tonnes moved), the truck should be assigned to the shorter route to maximize production. When the optimizer is configured to take into account the actual haulage resources, the supply of trucks to longer routes will be lowered to ensure that short routes have greater coverage or flow.

## Slide 30: Linear Programming Layer
Match Trucks
Setting Match Trucks in LP Mine to Yes – This indicates to Optimizer to set the Required Trucks value to the same value as the Actual Trucks available.
We are telling LP “we don’t have enough trucks to fully cover all of the circuits”, because Optimizer always wants to maximize production, it will therefore use the limited haulage in the most productive way, by covering the short routes first, Longer (less productive) routes will be covered last, which may result in some shovels going under or unused.
Notes: If the mine does not have enough trucks Ready to meet the current dig rate, setting Match Trucks in LP Mine to Yes will indicate to Joptimizer to set the Required Trucks value to the same value as the Actual Trucks available. This total truck haulage constraint will automatically decrease feed rates to low priority or long haul shovels and favour the short routes within the mine.
For example, if you have 5 trucks and 2 diggers and one route is 2 km long and the other is 10 km long, to maximise production (tonnes moved) you would assign the trucks to the shortest route. Doing this over a period of time would naturally move more material. Therefore, when running with Match Trucks on, Joptimizer will reduce feeds to the longer routes to ensure better coverage is made of the shorter routes or closer path shovels.

## Slide 31: Linear Programming Layer
LP Solution Procedure – create LP nodes
Notes: Based on the node attributes created earlier, we now have to create different lists of nodes. We do this based on the type of node as we saw before each node has a node type, which can be:
LPNODE_SHOVEL, for shovels
LPNODE_CRUSHER, for crushers
LPNODE_STOCKPILE, for Stockpiles
LPNODE_DUMP for dumps
If we define the structure of a mine as a network of nodes interconnected by routes, as discussed earlier, and if the objective of our optimizer is to find the most efficient flow rate for each route then we can see how it is necessary to analyze each node and the parameters that compose it.
For this we need to create a list of load nodes for shovels and another list of dump nodes because there are attributes or parameters that will affect or be specific to each.
As we can see in the Figure, in creating LP nodes the system looks for all the nodes in the database, and depending on the type of node, each node is added to either the list of load nodes or the list of dump nodes.
For load nodes it is necessary to analyze the material being loaded. If there is no grade selected the shovel priority will be configured as disabled, which will obviously affect trucks that will be assigned to such a shovel (the only way to send trucks to a disabled shovel is by making fixed allocations (or locking) trucks to the shovel). Grades for a shovel configuration in particular is crucial for the shovel to be considered in the LP calculation.

## Slide 32: Linear Programming Layer
LP Solution Procedure – restrictions
Configurable restrictions for a shovel are basically a list of locations of Dump destinations.
Any load node may be restricted from different types of dump nodes such as: crushers, stockpiles or dumps.
The result of a constraint will be that the route between the load node with restriction to the particular dump node will be not considered a feasible path for the LP solution.

## Slide 33: Linear Programming Layer
LP Solution Procedure – feasible routes
Check shovel priority
No feasible route created for unused shovels
Check shovel dump locks
If shovel is locked to dump, feasible route is created
Check grade and dump status
Dump must be Ready and accept material related to shovel grade
Check restrictions
No feasible route created if shovel restricted from dump
Notes: In the previous steps we created a list of the load and dump nodes based on their node types and also to modify the priorities of any shovel having no grade associated. If we think of a route is a series of paths or roads connecting two nodes we can see why it is necessary first all analyze the nodes.
Given that we have created the load nodes, to create feasible routes we have to analyze each dump and create possible routes as per the diagram.
First the system checks the priority of the shovel, if this is unused an error message will be sent and no feasible route will be created. Next check if the load node or shovel is fixed or locked to a dump node. If the shovel is locked to a dump, and the dump exists, then create the feasible route from the shovel to the dump in question. Then the next shovel is analyzed.
In the event that the shovel node was not locked to a dump then proceed to check the grade for the shovel. Based on the dump node to which the grade should be transported to check that, first, the dump node is in Ready, and second, that the material related to the grade is accepted by the dump node.
With this section we touched two important points relating to the tasks of the Dispatcher. One of them is at the start of the day, where it is recommended to check the States not only of the dump locations that will be used during the shift, but also the States of shovels, trucks, auxiliary equipment, workshops and others. The other point to consider is to highlight the importance of taking great care in the configuration of materials accepted at various dump locations since this directly affects the creation of feasible routes.
To better understand the creation of routes, we have to consider that when you create Shovel-Dump routes, it is necessary to take certain considerations. Materials are listed based on the shovel and the dump, and shovel grades related to the shovel and checked if they are accepted in the dump node, if they are not accepted the route is simply not created. It is also necessary to check that there are no restrictions of the shovel towards the dump node, if there are restrictions the routes would not be created. If it complies with the above conditions then you create routes related to the loading and dump node based on materials associated with the load node.
Feasible routes are also created from dump nodes to load nodes. Basically all dumps of the solution are analyzed and observed that they are not categorized as unavailable. For each such dump the system will find shovels not marked as unused, and on that basis the necessary routes are created. The shovel could have been marked as unused if dumps that accept the type of material were not in an operating state.
At the end of this process we have as a result a set of feasible routes based mainly in the States of dumps, materials and grades produced by shovels, as well as the restrictions of shovels to certain dump locations.
Factors affecting the creation of feasible routes:
Destination restrictions
Material/grade restrictions
State of destination
We see therefore how important checking it is for the dispatcher to check restrictions and dump states since these directly affect the creation of feasible routes.

## Slide 34: Linear Programming Layer
LP Solution Procedure – initialize array of constraints
Based on the feasible routes created above, which in turn were based on the creation of constraints and nodes, in this step the procedure initializes the array of restrictions. As already explained the linear programming algorithm maximizes the result, based on a given set of input variables and constraints.
At this point an array of constraints based on the feasible routes created in the previous step is initialized. Later we will add more restrictions related to each route to complete the array and create a solution to calculate an optimum feed rate for each existing route.

## Slide 35: Linear Programming Layer
LP Solution Procedure – continuity constraint
This step first analyses load nodes and subsequently dump nodes.
First, all the Ready shovels and dump nodes are collected, then the number of paths for each node are counted (both routes from the node, and the routes to the node).
To complete this step the array of constraints is added to, based on the feasible routes previously initialized.
The basic constraint at each node is continuity and establishes that the total flow to one shovel or dump must be equal to the flow from that shovel or dump.

## Slide 36: Linear Programming Layer
LP Solution Procedure – capacity constraint
Shovel Capacity
Also called LP feed rate
The rate at which the shovel could load 'standard trucks‘ including spot time
Adjust for Target Dig Rate
If TDR > capacity, set capacity = TDR
Adjust for Desired Coverage
Desired Coverage x Capacity
Based on average dig rate and spot time
Notes: For each load node, it is necessary to determine what rate the shovel can dig; based on this rate of excavation it is necessary to create a capacity requirement associated with the route that the shovel is using.
First for each load node it is necessary to calculate a capacity value based on several variables, namely:
Truck size, (truckSize), standard size of truck
Dig rate
Spotting time
Based on these variables the value of capacity is defined as:
For example, if we consider the following values:
Truck size = 225 tonnes, Dig rate = 3,000 tonnes per hr, Spotting time = 40 sec
We would have a capacity of 2,612 tonnes per hr.
If the Spotting time increased to 60 seconds, we would get a (lower) capacity of 2,454 tons per hour.
If on the other hand the Spotting time decreased to 30 seconds, we would see that the calculated capacity would be increased to 2,700 tonnes per hour.
The value of capacity is not the exact value that is inserted into the array of constraints, rather we need to consider two additional factors, namely Coverage Percentage and Target Dig rate.
Having already calculated for the capacity of the load node we compare this with the target dig rate value, if the latter is greater than capacity calculated, then our capacity will be matched to the Target Dig Rate. This makes sense if we think that on many occasions the haulage resources cannot satisfy the Target Dig Rate (i.e. shovel is undertrucked), however, one of the objectives of the optimizer is to try to reach those rates of excavation. Therefore when it gets a capacity based on the current dig and spotting time rate and this is less than the target dig rate set for each shovel, it is a good idea set up our array of requirements based on the Target Dig Rate.
Another important factor is the desired percentage of coverage. The desired percentage of coverage multiplies the capacity calculated above, and depending on the value of this, the Capacity requirement may increase or decrease. Basically, if you have for example a percentage of coverage of 130%, and a Rated capacity of 1,000 tons per hour, the coverage requirement to store in the array of constraints will be 1,300 tons per hour.
If you have a desired coverage of less than 100 %, the system creates two routes, one primary and one secondary. Both routes are fed to the constraints matrix and both may compete for being the neediest route however for a given node the primary route will be preferred, however it could be the case where you have enough haulage resources, the secondary path of a load node with one capacity requirement greater than the secondary route of another node will be preferred as the neediest route.
As we will see in the assignment layer section the load nodes capacity determine the haulage required and which routes have a greater need of haulage equipment. On that basis we can determine that the desired percentage of coverage of one shovel has a direct influence on the capacity requirements created for routes associated with that node.
Capacity requirements for dump nodes are also created. In this case the Coverage percentages are always 100% and the capacity is determined as the setting of capacity in tons per hour. This value has more sense when one speaks of crushers since these have a maximum processing limit of tonnes per hour.
In general, we can conclude that for the creation of capacity constraints these are the important variables and parameters to consider: Desired Percentage coverage, Target dig rate for shovels and Capacity for dumps.
These values directly affect the creation of capacity constraints, increasing or decreasing the capacity requirements for each path and node, thus affecting the determination of the neediest route and the neediest shovel which in turn have a large weight in the allocation of trucks as is discussed later.
Also note that the system considered the spotting times and dig rates calculated in real time, and this in turn affects the coverage requirement. Spotting time, as we have seen, affects the ability of a load node such that lower spotting times will result in more capacity. Similarly higher dig rates and higher Desired coverage of a load node will increase the Capacity in tons per hour, and the haulage requirement will be increased, favoring to the route in question when determining the neediest route.
For each load node, it is necessary to determine what rate the shovel can dig; based on this rate of excavation it is necessary to create a capacity requirement associated with the route that the shovel is using.
First for each load node it is necessary to calculate a capacity value based on several variables, namely:
Truck size, (truckSize), standard size of truck
Dig rate
Spotting time
Based on these variables the value of capacity is defined as:
𝑆ℎ𝑜𝑣𝑒𝑙 𝐶𝑎𝑝𝑎𝑐𝑖𝑡𝑦=(𝑆𝑡𝑎𝑛𝑑𝑎𝑟𝑑 𝑡𝑟𝑢𝑐𝑘 𝑠𝑖𝑧𝑒)/(〖(𝑠𝑡𝑎𝑛𝑑𝑎𝑟𝑑 𝑡𝑟𝑢𝑐𝑘 𝑠𝑖𝑧𝑒〗∕〖𝑑𝑖𝑔 𝑟𝑎𝑡𝑒)+(〖𝑠𝑝𝑜𝑡 𝑡𝑖𝑚𝑒〗∕〖3600)〗〗)
For example, if we consider the following values:
Truck size = 225 tonnes, Dig rate = 3,000 tonnes per hr, Spotting time = 40 sec
We would have a capacity of 2,612 tonnes per hr.
If the Spotting time increased to 60 seconds, we would get a (lower) capacity of 2,454 tons per hour.
If on the other hand the Spotting time decreased to 30 seconds, we would see that the calculated capacity would be increased to 2,700 tonnes per hour.
The value of capacity is not the exact value that is inserted into the array of constraints, rather we need to consider two additional factors, namely Coverage Percentage and Target Dig rate.
Having already calculated for the capacity of the load node we compare this with the target dig rate value, if the latter is greater than capacity calculated, then our capacity will be matched to the Target Dig Rate. This makes sense if we think that on many occasions the haulage resources cannot satisfy the Target Dig Rate (i.e. shovel is undertrucked), however, one of the objectives of the optimizer is to try to reach those rates of excavation. Therefore when it gets a capacity based on the current dig and spotting time rate and this is less than the target dig rate set for each shovel, it is a good idea set up our array of requirements based on the Target Dig Rate.
Another important factor is the desired percentage of coverage. The desired percentage of coverage multiplies the capacity calculated above, and depending on the value of this, the Capacity requirement may increase or decrease. Basically, if you have for example a percentage of coverage of 130%, and a Rated capacity of 1,000 tons per hour, the coverage requirement to store in the array of constraints will be 1,300 tons per hour.
If you have a desired coverage of less than 100 %, the system creates two routes, one primary and one secondary. Both routes are fed to the constraints matrix and both may compete for being the neediest route however for a given node the primary route will be preferred, however it could be the case where you have enough haulage resources, the secondary path of a load node with one capacity requirement greater than the secondary route of another node will be preferred as the neediest route.
As we will see in the assignment layer section the load nodes capacity determine the haulage required and which routes have a greater need of haulage equipment. On that basis we can determine that the desired percentage of coverage of one shovel has a direct influence on the capacity requirements created for routes associated with that node.
Capacity requirements for dump nodes are also created. In this case the Coverage percentages are always 100% and the capacity is determined as the setting of capacity in tons per hour. This value has more sense when one speaks of crushers since these have a maximum processing limit of tonnes per hour.
In general, we can conclude that for the creation of capacity constraints these are the important variables and parameters to consider: Desired Percentage coverage, Target dig rate for shovels and Capacity for dumps.
These values directly affect the creation of capacity constraints, increasing or decreasing the capacity requirements for each path and node, thus affecting the determination of the neediest route and the neediest shovel which in turn have a large weight in the allocation of trucks as is discussed later.
Also note that the system considered the spotting times and dig rates calculated in real time, and this in turn affects the coverage requirement. Spotting time, as we have seen, affects the ability of a load node such that lower spotting times will result in more capacity. Similarly higher dig rates and higher Desired coverage of a load node will increase the Capacity in tons per hour, and the haulage requirement will be increased, favoring to the route in question when determining the neediest route.

## Slide 37: Linear Programming Layer
Shovel Capacity Example Calculation
Standard truck size 225 t
Dig rate 3,000 tph
Spotting time 40 secs
  If spot time increased to 60 secs, capacity would be 2,454 tph
Convert from seconds to hours
Load time for standard truck at current dig rate

## Slide 38: Linear Programming Layer
LP Solution Procedure – current haulage
To get the current hauling for each node and route, and their associations to pits and regions, first the following parameters are obtained from our database:
  Assigned Shovel
  Shovel locks
  Hauling from shovel
  Truck size
Current Haulage
Trucks hauling from shovel
Trucks assigned to shovel
Truck size
Shovel locks
Notes: In the assignment layer that we will study later, to determine the neediest route and the neediest shovel, which are the route and shovel with greatest haulage needs; the required hauling and current hauling values are used.
Required hauling is obtained on the basis of the capacity requirements, and current hauling is obtained from assigned haulage resources.
To get the current hauling for each node and route, and their associations to pits and regions, first the following parameters are obtained from our database:
Assigned Shovel
Shovel locks
Hauling from shovel
Truck size
The Id of assigned shovel and the shovel locks comes from looking for all assignments of trucks to each shovel which are registered in the database in the mapping table. The trucks hauling from shovels is obtained from the hauling table in our database, where the information is trucks traveling loaded from a shovel to a dump.
The value of Truck size is the size of truck related to each specific truck, not to be confused with the Standard Truck Size that is defined for LP overall. The value we are interested in is defined for each truck and comes from the table of equipment from our database.
Once this information is gathered for the load node related to the either to the id of the Assigned, locked shovel or hauling from shovel the value of current hauling is increased based on the size of truck for the load node. This gives the result of the value of the current haulage for each load node.
Now with the load nodes and their respective haulage values, create lists of hauling routes related to these load nodes. This is necessary if we remember that the columns of our matrix of constraints are based on the feasible routes, so they have to establish the hauling requirements on the basis of the routes to be able to store them in the array of constraints. During this process it also stores the pits to which the Dump nodes belong, giving the possibility of hauling requirements for each pit existing in the mine.
The current hauling value basically represents the number of trucks that are related to each feasible route, based on the sizes of trucks associated with the load node of the route. Having these haulage requirements, which are basically the current trucks on each route, and thus on each load node, you can tell the difference between current haulage and required haulage to determine routes and shovels with major transportation needs.

## Slide 39: Linear Programming Layer
LP Solution Procedure – hauling route rates
Where truck exchange time is defined as follows:
If the node is loading = spotting time + loading time for standard truck.
If the node is dump = spotting time + tipping time (60 sec).
Notes: Finally hauling rates for each route are calculated. This is done using the Capacity requirements previously obtained. Within this process importantly haulage required for each shovel is calculated. For this are considered the following factors:
Capacity requirement
Travel time
Spotting time
Capacity is obtained for each route and required haulage is estimated using the following formula:
When the target node is loading:
Where truck exchange time is defined as follows:
If the node is loading = (spotting time + (std truck size/capacity)/3600
If the node is a Dump = (spotting time + 60)/3600
When the target node is a Dump:
Required haulage = capacity * (travel time + spotting time)/ 3600)
Finally hauling rates for each route are calculated. This is done using the Capacity requirements previously obtained. Within this process importantly haulage required for each shovel is calculated. For this are considered the following factors:
Capacity requirement
Travel time
Spotting time
Capacity is obtained for each route and required haulage is estimated using the following formula:
When the target node is loading:
𝑅𝑒𝑞𝑢𝑖𝑟𝑒𝑑 𝐻𝑎𝑢𝑙𝑎𝑔𝑒=𝐶𝑎𝑝𝑎𝑐𝑖𝑡𝑦 𝑥 (travel time + truck exchange time)/3600
Where truck exchange time is defined as follows:
If the node is loading = (spotting time + (std truck size/capacity)/3600
If the node is a Dump = (spotting time + 60)/3600
When the target node is a Dump:
Required haulage = capacity * (travel time + spotting time)/ 3600)

## Slide 40: Linear Programming Layer
Required Haulage Example Calculation
Shovel capacity 3,750 tph
Spotting time 20 secs
Std truck size 180 t
Travel to dump 750 secs
Travel from dump 700 secs
Dump to shovel path
Truck exchange time = 20 + 3600 * (180/3750) = 192.8 secs
Which gives 930 tonnes, or 5.2 standard trucks
Shovel to dump path
Truck exchange time = 20 + 60 = 80 secs
Which gives 864 tonnes, or 4.8 standard trucks
Total haulage required for the shovel will be 930 + 864 = 1,794 tonnes, or 10 standard trucks.
Convert from seconds to hours

## Slide 41: Linear Programming Layer
LP Solution Procedure
The result is the definition of hauling rates for each route, since such hauling rates are used by the Dynamic Assignment Layer to determine future allocations for each truck.

## Slide 42: Linear Programming Layer
LP Recalculation
Due to the ever-changing nature of the mining environment, the optimal feeding rates of routes must be recalculated when certain trigger events occur to ensure that the LP solution is optimal.
Status changes
  If a shovel changes status LP recalculates (if the status changes to Ready and the shovel has trucks in its queue in delay, then the system changes the trucks to Ready if the readyTrucksAtShovel variable's Configuration is YES).
  When a Dump node changes to State which is not operating.
Change of grade in a shovel.
Change of shovel locks.
Change of shovel priority.
Change of desired percentage coverage of a shovel.
Material change on a dump.
Changes to shovel-splits.
Notes: Note: Truck changes status does not trigger an LP recalculation; however it does cause the system to perform truck allocations.
If we recall the LP solution procedure, we can see clearly that if there is a change in the desired percentage of coverage or shovel priority for example it would be necessary to perform a recalculation of the LP solution, since the percentage of coverage directly affects the capacity requirements for each shovel. In the case of the shovel priority, this affects the coefficient of Route priority, which in turn affects the perception that we have of the travel time of a specific route, making it shorter for shovels with higher priority thereby turning the route/shovel into a better option for my solution.

## Slide 43: The Dynamic Assignment Layer
Assignment types
Once Optimizer has all the information required from the LP layer, allocations of trucks can be used to optimize the production inside the mine and, at the same time, minimize cost, which in this case is the travel time.
Assignments types:
  Shovel assignments.
  Dump assignments.

## Slide 44: The Dynamic Assignment Layer
Best Path
The calculation performed by the best route module (BP Best Path) is one of the more important calculations carried out in the assignments layer.
Dispatchers should make sure that the elevation of all call points, blasts and dumps are correct and valid. If this is not the case, then the optimizer may perform "wrong" assignments.
The travel time is the time in seconds of the trucks traveling on a given route, also the gradient, the average speed, and if the truck is traveling empty or loaded.

## Slide 45: The Dynamic Assignment Layer
Average Speeds and Road Categories
Each road segment is associated with a Road Category.
This information is stored in three dimensions (line or curve) and automatically calculates the total distance, empty/loaded travel times, and speed limits.
Road Categories are configured by the Hexagon PE in enums table.
This impacts on ETAs and truck average speeds either loaded or empty.
Mine Controllers must associate each road segment when creating new roads.
Average speeds table is constantly updated as different trucks types travel through showing truck’s speed on that road category and gradient, loaded or empty.
The table contains average speed for each gradient and road category for each truck type loaded and empty.
There are two types road categories:
Haul Roads
Pit Roads
Notes: JIGSAW stores information for each road segment connecting two locations in three dimensional space (using either a line or a curve) and automatically calculates the total distance, empty/loaded travel times, and speed limits
The average speeds table is constantly updated as trucks travel the network. The average speeds table contains the average speed for each gradient and road category for each truck type loaded and empty. Each time a truck traverses a road segment, the average speeds table is updated to include the speed for that truck’s type on that road category and gradient, loaded or empty.
Each road segment is associated with a Road Category. Road Category example include;
Haul Roads
Pit Roads
Road categories are configurable and can be changed by a Project Engineer on site or remotely using the enums interface within Jigsaw.
Once the set of road categories has been decided upon, the Mine controllers, when creating roads must choose the Road Category the segment belongs to.
This will have an impact on the ETAs and average speed for the road network.
Internally the system stores an average speed for each Road Category depending on the trucks being loaded or empty and by the PCT Grade.
To clarify this, if we have two roads, road A and B and road A has a percentage grade of 4 and road B has a percentage grade of 2 and both roads have been defined in the same road category then average speeds would be stored for both roads twice, once for empty movement along the road and once more for loaded movement.
The more percentage grades we have for a given road category the more average speeds that are stored.
The average speed is stored for each equipment type and is a moving average over the four last reads.
So correctly categorizing road category is important as otherwise you could have a slow road (Tiedown Road) with a fast average speed if it has been categorized as a Haul Road.
Using these average speeds and given the length and percentage grades of all the road segments that make up a path between locations, the system can return an accurate ETA on a trucks arrival given a loaded or empty state.

## Slide 46: The Dynamic Assignment Layer
Important Points
Since average speeds are calculated by road category, road categories are important and care should be taken to assign the correct category to a new road when it is created.
Average speeds are not weight averages i.e. a 50 m length of road will affect the average speed just the same as a 5000 m long road.
Gradients of road segments are determined by the elevations of their end points in the database, not by GPS (although the Road Elevations tool can be used to do this). Therefore if a road is incorrectly created with a 0% gradient, it is the 0% gradient average speed which is used to calculate truck ETA’s (and it is the 0% average speed which is updated as trucks travel the segment).
Over time if incorrect call point elevations are used, the average speeds will become ‘corrupt’ i.e. not reflective of reality. It is possible to reset the average speeds within OP Pro Manager and this should be done as a matter of routine.
Notes: The average speed is stored for each equipment type and is a moving average over the four last roads. So correctly categorizing the road category is important as otherwise you could have a slow road (Tiedown Road) with a fast average speed IF it has been categorized as a Haul Road.
As a truck travels, the system calculates its estimated time of arrival (ETA) at its assigned destination using the best path and the average speeds for each road segment along the best path. The ETA is obviously vital in forecasting the shovel hang and truck queue times which drive the truck assignment algorithms.

## Slide 47: The Dynamic Assignment Layer
Important Points
Notes: The average speed is stored for each equipment type and is a moving average over the four last roads. So correctly categorizing the road category is important as otherwise you could have a slow road (Tiedown Road) with a fast average speed IF it has been categorized as a Haul Road.
As a truck travels, the system calculates its estimated time of arrival (ETA) at its assigned destination using the best path and the average speeds for each road segment along the best path. The ETA is obviously vital in forecasting the shovel hang and truck queue times which drive the truck assignment algorithms.

## Slide 48: The Dynamic Assignment Layer
Shovel Assignments
Shovel assignments
Find neediest shovel
Find neediest route
Find the truck with least cost
Check truck restrictions
Notes: These allocations are calculated much before being required. The optimizer has information about which will be the next shovel that all trucks will be assigned until this information is required. When a truck requests a new assignment, for example after Dumping, the allocation to the next shovel, previously calculated for the truck, it is used for such assignment.
Broadly speaking, we can summarize the allocation process in the following blocks:
Neediest shovel
Neediest route
Truck with least cost
Truck restrictions
First the neediest shovel is calculated. This is the shovel with a greatest need for trucks and probably the shovel with the highest priority. Next the neediest route is calculated from the routes belonging to the neediest shovel. Next the truck with lowest cost of assignment is found and after checking restrictions the assignment will take place.

## Slide 49: The Dynamic Assignment Layer
Shovel Assignments - Neediest Shovel
By shovel idle time
Not Low priority
IF shovel has been idle for > assignbyidle THEN neediest
By Haulage Need
LP required and Actual Haulage
Shovel with greatest difference is neediest

## Slide 50: The Dynamic Assignment Layer
Shovel Assignments - Neediest Shovel - Assign by Idle
Shovel Capacity
If more than 1 shovel is idle then shovel with highest capacity is neediest
NOT LOW
Shovel Priority
Shovel idle (hang) time
Must be more than assignbyidle
Notes: The process to find the neediest shovel is described in Figure 8. First of all we will have to observe the shovel priority and the idle time. If the idle time is greater than the assignByIdle configuration variable and the priority is not Low (i.e. Normal or High), then the calculation of the neediest shovel will be based on the idle time and the feed rate.
The process then calculates the multiplication of the calculated idle time and the feed rate of the shovel and the resulting value is compared with the corresponding values of other shovels to fulfil these conditions, and the neediest shovel is the one that has the largest value.
The configuration assignByIdle (set at 180 seconds by default) gives preference to the shovels that have had more time waiting for trucks (idle time). Where more than one shovel has been waiting Joptimizer takes into account each shovel’s wait time and feed rate in determining which shovel to make the neediest. This is provided the priority of the shovel is Normal or High, if the priority of the shovel is low the shovel is not considered in this part of the truck assignment process.

## Slide 51: The Dynamic Assignment Layer
Shovel Assignments - Neediest Shovel - By Haulage Need
Shovel Priority and Desired Coverage
Set by dispatch, according to the daily plan
Higher priority will have a greater chance of getting trucks
Trucks required and current trucks
Greater difference between required and current = greater need
Shovel Delays
Optimizer reduces the need based on the expected length of the delay

## Slide 52: The Dynamic Assignment Layer
Shovel Assignments - Neediest Shovel - By Haulage Need - Shovel Priority Factor
The Shovel Priority Factor is calculated based on the shovel percentage of cover and the shovel priority
For example, with Desired Coverage 100 % and Shovel Priority High; Shovel Priority Factor would be 1.00 x 1.25 = 1.25
Shovel priority
High=1.25
Normal=1.00
Low=0.75
Notes: Once the shovel priority factor is calculated, this factor is multiplied by the required haulage for the shovel, previously calculated in the LP layer. As the shovel priority factor increases so too will the required haulage.

## Slide 53: The Dynamic Assignment Layer
Shovel Assignments - Neediest Shovel - By Haulage Need - Total Haulage
Required Haulage
Adjusted for Shovel Priority Factor
Current Haulage
‘Total Haulage’
Notes: The value of total haulage is driven by the difference between required and current haulage
Note that Required is adjusted for Shovel Priority Factor, therefore shovels with higher SPF will have a higher ‘required haulage’ value

## Slide 54: The Dynamic Assignment Layer
Shovel Assignments - Neediest Shovel - By Haulage Need - Need Ranking
Shovel 1 Total Haulage
Shovel 2 Total Haulage
Shovel 3 Total Haulage
Need Rank 1
Need Rank 2
Need Rank 3
‘Total Haulage’
Notes: Shovels are ranked by their total haulage value, with the highest value being given the higher rank

## Slide 55: The Dynamic Assignment Layer
Shovel Assignments - Neediest Shovel - By Haulage Need - Example
Shovel | Desired coverage | Priority | Shovel Priority Factor | Required haulage | SPF * Required | Current haulage | Total Haulage | Need ranking
01 | 100%=1.0 | High=1.25 | 1.25 | 8.50 | 10.63 | 8.50 | 2.13 | 3
02 | 90%=0.9 | Normal=1.00 | 0.90 | 6.50 | 5.85 | 2.50 | 3.35 | 1
03 | 110%=1.1 | Low=0.75 | 0.83 | 10.00 | 8.30 | 5.00 | 3.30 | 2

## Slide 56: The Dynamic Assignment Layer
Shovel Assignments - Neediest Route
The neediest route is the route most in need of haulage.
To find the neediest route first, Optimizer finds all routes to the neediest shovel.
Then for each route, get the required haulage, and subtract from this value the current haulage assigned to this route.
So the neediest route is the route to the Neediest Shovel which has the greatest difference between Required and Actual Haulage.

## Slide 57: The Dynamic Assignment Layer
Truck with least cost
Neediest shovel
Truck 1
Truck 2
Truck 3
For each truck
  How long to travel to shovel.
  How long will it wait when it gets there.
  Forecasts ETAs for all trucks.
  Total cost is calculated based on travel and wait times.
  By default, travel time is 1.5 times more ‘expensive’ than idle time.

## Slide 58: The Dynamic Assignment Layer
Assigning trucks
Neediest shovel
Lowest cost truck
Truck assignment
Notes: Recap

## Slide 59: The Dynamic Assignment Layer
Dump Assignments
Trucks get assignments to dumps when they are finished loading and when they begin hauling:
  When a truck enters the hauling activity this generates a request for a dump assignment.
  The function will verify if there are dump locks in the truck, shovel, or Material that was loaded the truck, and the Truck will be assigned to such fixed assignment only if the dump accepts the type of material loaded.
  If there is a fixed assignment, then the system checks all dumps connected to the shovel and use the Dump most appropriate based on the current restrictions.
  If no dump is found in the previous step, then the system will look for the closest dump and assign the truck there.
  Note that all truck assignments are updated at this point, and the ‘next shovel’ value may change. This stored value is used as the truck assignment if the truck is out of communication when it needs an assignment.

## Slide 60: The Dynamic Assignment Layer
Truck Reassignments
Truck reassignments may be needed to account for a change in the conditions of the mine since the previous assignment was made. Depending on the operational structure of the mine there may be a need to configure reassignment points at specific beacons within the road network, for example at key intersections.
OP Pro can perform truck reassignments both manually and automatically:
  Manual assignments can be performed by a Dispatcher reassigning a truck toward a different shovel, or the operator of the truck can request a reassignment from their panel (this option may not be enabled in different mines for operational reasons).
  The system can also handle automatic reassignments and this is mainly done in two ways:
    Reassignment beacons.
    Misroutes.

## Slide 61: The Dynamic Assignment Layer
Truck Reassignments - reassignment process
shovels ahead of truck
without backtracking from reassignment point
remove ineligible shovels
disabled
best cost
travel and idle costs
restricted
queue capacity
Notes: The system detects that a truck is on a road that ends at a reassignment callpoint and immediately analyzes the reassignment process.
The reassignment process first of all gets the current position of the truck in order to determine the possible shovels to which the truck can be reassigned ‘ahead’ of the truck. One of the conditions for a shovel to be considered as eligible is that the shovel must be in a location that the truck can travel to from it’s current location without having to travel in the opposite direction or back track. This is possible in our system because we know not only the position and speed of the truck, but our algorithms also detect the direction in which the truck is traveling.
After finding the set of eligible shovels, the system discards shovels based on the following conditions:
Shovel disabled
Shovel with restrictions
Shovel with too many trucks in queue (queue capacity will be exceeded when truck arrives)
If a shovel is disabled the system does not consider it as a viable option for the reassignment. In the same way, if the truck is restricted from such a shovel, or there is a restriction of the material that the shovel is loading, or other existing restrictions, the shovel will not be considered as eligible. Also if the system finds that the shovel has too many trucks in its queue, or will have too many trucks in its queue at the time of the arrival of the truck to be assigned, the system will determine that the shovel is not eligible.
Once there is a list of eligible shovels the next step in the reassignment process of is to analyze the cost of each of the options, as well as determine which is the best shovel based on such cost. The system analyses the cost associated to each shovel and the associated route and compare each of them in order to find the lowest cost and hence the best shovel.

## Slide 62: The Dynamic Assignment Layer
Reassignments - Shovels ahead
Question 1:
(a) Which shovels are ‘ahead’ of CP 1?
(b) And CP 2?
Question 2:
(a) If EX1010 is disabled, which shovels are ahead of CP 1?
(b) And CP 2?
CP 1
CP 2
Notes: 1 (a) only EX1008
1 (b) both EX1008 an EX1010
2 (a) only EX1008
2 (b) only EX1008

## Slide 63: The Dynamic Assignment Layer
Reassignments - Ineligible Shovels
Firstly, the shovel must not have a ‘disabled’ priority to be considered in the reassignment.
Similarly, if the shovel or truck has restrictions which would prevent the truck assignment.
Optimizer forecasts the truck ETA at each shovel and predicts the situation at that time.
If the shovel has a queue capacity set, and assigning the truck from the reassignment point would result in the queue capacity being exceeded (at the time of the truck’s ETA), then the shovel will not be considered for reassignment.
Notes: 1 (a) only EX1008
1 (b) both EX1008 an EX1010
2 (a) only EX1008
2 (b) only EX1008

## Slide 64: The Dynamic Assignment Layer
Truck Reassignments - Reassignment process - calculation of the best cost and best shovel
Travel time
Travel cost (configuration)
Queue time
Idle cost (configuration)
Shovel Priority Factor
Priority x Desired Coverage
Reassign cost (configuration)
Notes: First Joptimizer finds the value associated with the configurable variable idleCost. This value is used to calculate a cost for forecast truck idle (queue) time. The default value of idleCost is 1.0, and its main function is to directly influence the calculated cost of truck idle, to thus increase or decrease the weight that idle time has in the calculation of the best cost. As can be seen from the figure this value is stored in the variable Cost A.
Having obtained Cost A (idle cost), the system compares the current assigned shovel, and the possible shovel to use for reassignment (i.e. the shovel option being costed), to determine if they are the same shovel. If the shovels aer not the same, the system increments the Cost A based on the value of the variable reassignCost.
The variable reassignCost is configurable and its default value is 180. If you look at the formula Cost B= Cost A + reassignCost, we can determine the main function of the variable reassignCost is to affect the perception of the queueing time that exists in certain shovel. By default, it increases the queuing time for the truck to be reassigned by 3 minutes, which makes the system prefer to not assign the truck to a different shovel.
Now we find ourselves with the calculation of the Shovel Priority Factor. This factor considers the Desired Coverage and the Shovel Priority, both values can and must be set according to the priority that you want to give to each shovel.
The priorities of shovels is defined as follows:
High, value = 1.25
Normal, value = 1.00
Low, value = 0.75
So if for example we have a shovel with a Desired Coverage of 100%, and a shovel priority set to High, we would get a Shovel Priority Factor by 1.00 X 1.25 = 1.25.
If you look at the formula for Cost C in Figure 12, we can determine that the Cost C decreases as the shovel priority factor increases. In this way shovels with higher priority and higher desired coverage settings are seen by Joptimizer as having a lower cost and therefore more attractive for truck reallocations.
Finally bit also importantly Joptimizer takes into account the truck travel times. The travel time and the travelCost are the last parameters that affect the best cost used to determine the best shovel to which the truck will be reassigned.
The travelCost, which is configurable and by default it has a value of 1.5 is multiplied by the calculated travel time given by Best Path to a given shovel, thus changing the value of travel time that is used in the calculation of the reassignment.
The end best cost formula is:
Best cost = Cost C + travelCost * travel time.
The effect of the travelCost if we use the value by default, is to increase the travel time by 50%. The value of travelCost is higher than that of idleCost since trucks consume more cost when traveling as opposed to queuing.
The relative cost of travel and idle times will cause Joptimizer by default to favor routes that have shorter travel times.

## Slide 65: The Dynamic Assignment Layer
Truck Reassignments - Reassignment process - calculation of the best cost
Cost A
(Idle cost)
Truck ETAs and load times are used to predict the total idle (queue) time at the shovel if the assignment was made.
Idle time is multiplied by the configured idlecost (default 1.0)
Cost B
(Reassign cost)
If the assignment being evaluated is to a shovel which is not the truck’s current assignment, reassignCost (default 180) is added.
Cost C
(Shovel Priority Factor)
Shovel Priority Factor = Shovel Priority x Desired Coverage
Cost A or Cost B is divided by SPF, such that higher priority or coverage shovels will have a lower cost C
Travel Cost
Truck travel time x travelcost (default 1.5)
Total Cost
Cost C + Travel cost
Notes: Having obtained Cost A (idle cost), the system compares the current assigned shovel, and the possible shovel to use for reassignment (i.e. the shovel option being costed), to determine if they are the same shovel. If the shovels are not the same, the system increments the Cost A based on the value of the variable reassignCost.
The variable reassignCost is configurable and its default value is 180. If you look at the formula Cost B= Cost A + reassignCost, we can determine the main function of the variable reassignCost is to affect the perception of the queueing time that exists in certain shovel. By default, it increases the queuing time for the truck to be reassigned by 3 minutes, which makes the system prefer to not assign the truck to a different shovel.
Now we find ourselves with the calculation of the Shovel Priority Factor. This factor considers the Desired Coverage and the Shovel Priority, both values can and must be set according to the priority that you want to give to each shovel.
The priorities of shovels is defined as follows:
High, value = 1.25
Normal, value = 1.00
Low, value = 0.75
So if for example we have a shovel with a Desired Coverage of 100%, and a shovel priority set to High, we would get a Shovel Priority Factor by 1.00 X 1.25 = 1.25.
If you look at the formula for Cost C in Figure 12, we can determine that the Cost C decreases as the shovel priority factor increases. In this way shovels with higher priority and higher desired coverage settings are seen by Joptimizer as having a lower cost and therefore more attractive for truck reallocations.
Finally bit also importantly Joptimizer takes into account the truck travel times. The travel time and the travelCost are the last parameters that affect the best cost used to determine the best shovel to which the truck will be reassigned.
The travelCost, which is configurable and by default it has a value of 1.5 is multiplied by the calculated travel time given by Best Path to a given shovel, thus changing the value of travel time that is used in the calculation of the reassignment.
The end best cost formula is:
Best cost = Cost C + travelCost * travel time.
The effect of the travelCost if we use the value by default, is to increase the travel time by 50%. The value of travelCost is higher than that of idleCost since trucks consume more cost when traveling as opposed to queuing.
The relative cost of travel and idle times will cause Joptimizer by default to favor routes that have shorter travel times.

## Slide 66: The Dynamic Assignment Layer
Truck Reassignments - Reassignment process - Best Cost Calculation Example
Notes: Default settings for travel, idle and reassign cost
EX318 has longer travel time and more idle time forecast
Walk through Cost A, Cost B and Cost C then Travel cost and Total Cost
Truck is reassigned to EX319 because of lower total cost

## Slide 67: The Dynamic Assignment Layer
Truck Reassignments - misroutes
Misroute is raised when a truck heads down the wrong road segment or takes an incorrect turn at a given intersection.
Normally misroutes are configured when a truck heads more than 100m down incorrect road.
Optimizer then provides new assignment to the operator.
Road can also be configured not to report misroutes.
Mine Controller and operators are alerted when a truck is not on a road, the system will find the nearest road within off-road distance meters and consider the truck on this road.
By default this is set to 25 m. This means that a truck can be up to 25 m from a road before it is considered off-road.
If a truck is outside of this distance it is not considered traveling along a given road.
This value is configurable by Project Engineer if the default value cause issues.
Notes: Misroutes
These are raised when a Truck heads down the wrong road segment or takes an incorrect turn at a given intersection.
The system is configured to raise a misroute when a truck has headed more than 100m down an incorrect road.
This is configurable and an Project Engineer can set this for entire road network.
One property of roads is that they can be set not to report misroutes.
You may have a road that applies to this and therefore by setting a flag within the road properties, the road will not report misroutes.
Misroutes are used by the optimizer to provide the truck with a new assignment given the road it is now traveling down.
They can also be configured to be raised to the mine controller using the inbox.
Misroutes when triggered will also activate a buzz and a message to the operator of the given truck.
Offroad Distance One final configurable parameter of the road network is the variable that defines when a truck is marked as Off-road.
When a truck is not on a road, the system will find the nearest road within off-road distance meters and consider the truck on this road. By default this is set to 25 m.
This means that a truck can be up to 25 m from a road before it is considered off-road.
This value is configurable by a Project Engineer should the default value cause issues. If a truck is outside of this distance it is not considered traveling along a given road.

## Slide 68: The Dynamic Assignment Layer
Truck Reassignments - Fuel Assignments
Fuel assignment for a truck is generated whenever its fuel tank is below its corresponding fuel Low Percent entry in the Fuel Consumption table.
Optimizer only considers empty trucks for fuel assignments.
There are three input variables for automatic refuelling assignments, these are:
  Fuel Low Percent - when the fuel level reaches this Optimizer will assign to the nearest ready fuel bay when the current queue has not exceeded the limit.
  Fuel Empty Percent - when the fuel level reaches this Optimizer will ignore queue and assign to the nearest ready fuel bay.
  Fuelling Distance - trucks on or under the Low fuel percent are restricted from working outside this one way haul distance (if possible) to the assigned shovel.
Example: Variables used in determining fuel shop assignments are:
Fuel Low Percent = 18
Fuel Empty Percent = 13
Fuelling Distance = 5500
Notes: JoptimizerFuel generates a fuel assignment for a truck whenever its fuel tank is below its corresponding fuelLowPercent entry in the FuelConsumption table.
Trucks that are coming back from shovels are ignored in order to keep them from going to a fuel station with load. If the fuel tank level is above fuelEmptyPercent, fuel assignments are generated only if the queue at the available fuel station is below the configured maximum queue limit and if the fuel station is open. If the fuel tank level is below fuelEmptyPercent, the truck is assigned to the nearest fuel station regardless of the queue capacity at the station of the queue limit. Joptimizer uses fuelingDistance to prevent fuel assignments from large distances and it will try to keep the trucks low on fuel work close to a fuel shop. Variables used in determining fuel shop assignments are: Fuel Low Percent = 18 Fuel Empty Percent = 13 Fuelling Distance = 5500 Note: For the following logic, a refuel is considered critical if the truck is between Fuel Low Percent and Fuel Empty Percent.

## Slide 69: The Dynamic Assignment Layer
Truck Reassignments - TKPH - Overview
Large haul trucks are designed to haul heavy loads at high speed.
Heat build-up in tyres accelerate tire deterioration.
Can cause potential premature failures and in extreme cases explode or fire.
May pose safety risks to operators and personnel.
Operators and Mine Controllers should be aware tires are very expensive and tire management is very important to job sustainability.
TKPH is therefore a measurement of the workload on a tire and is used to maintain the operating conditions and prevent premature failure.
Mining tire manufacturers assign TKPH ratings to each tire based on size, construction thread type and rubber compound.
This rating is based on the weight of load and speed that tire can handle without overheating.
In the United States is it called Tons Mile Per Hour (TMPH).
Notes: Large haul trucks are designed to haul heavy loads at high speed.
Heat build-up in tyres may accelerate tyre deterioration and can cause potential premature failures and in extreme cases explode or fire which may pose a safety risk to operators.
If the mine is unable to prove that tyre heat has been maintained within acceptable range, they may lose on warranties.
Operators and Mine Controllers should be aware tyres are very expensive and tyre management is very important to job sustainability.
TKPH, Tons Kilometre Per Hour is therefore a measurement of the work load on a tyre and is used to maintain the operating conditions within warranty restrictions and prevent premature failure. Mining tyre manufacturers assign TKPH ratings to each tyre based on size, construction thread type and rubber compound.
This rating is based on the weight of load and speed that tyre can handle without overheating. In the United States is it called Tons Mile Per Hour (TMPH).

## Slide 70: The Dynamic Assignment Layer
Truck Reassignments - TKPH - Overview
If the calculated average TKPH is greater than the TKPH Warning Threshold for any of the tyres, the truck is flagged as having a TKPH warning.
Average TKPH value within the maintenance table is set, and truck KPI is updated with the highest TKPH average.
If there is a TKPH warning for the truck, the truck is assigned to shovels with small TKPH averages for the routes to that shovel.
If the TKPH assign in the database was 25%, the logic would restrict truck with TKPH warnings to the lowest 25% of the haulage cycles.
After deciding the shovel paths with the lowest TKPH cycles, the logic then fines the best option out of the available shovels.
The best shovel path is chosen by the distance required to travel to the shovel and the projected idle cost for the truck once it arrives in the shovel queue.
Optimizer computes average TKPH as a weighted average of all the empty paths entering the shovel and loaded paths leaving the shovel.
Notes: If the calculated TKPH Average is greater than the TKPH Warning Threshold for any of the tires, the truck is flagged as having a TKPH warning, the average TKPH value within the maintenance table is set, and the truck KPI is updated with the highest TKPH tire average.
If there is a TKPH warning for the truck, the truck is assigned to shovels with small TKPH averages for the routes to that shovel.
The routes available to the truck are based off of the TKPH assign percentage (set in the fuel consumption table).
If the TKPH assign in the database was 25%, the logic would restrict truck with TKPH warnings to the lowest 25% of the haulage cycles.
After deciding the shovel paths with the lowest TKPH cycles, the logic then fines the best option out of the available shovels.
The best shovel path is chosen by the distance required to travel to the shovel and the projected idle cost for the truck once it arrives in the shovel queue.
In addition to the TKPH logic that is computed as a truck travels a road segment, the TKPH average is also initialized for cases where the truck is not traveling or hauling.
In these cases, if specified by the enum attributes for the activity being performed, the truck is considered idling.
Joptimizer computes the average TKPH for each shovel as a weighted average of all the empty paths entering the shovel and loaded paths leaving the shovel.
The computed TKPH for each path is weighted based upon the total feed rate to the shovel.
Thus, if a shovel is fed 50% from dump A and 50% from dump B, each path to the shovel would contribute 50% to the total weighted TKPH value.
These TKPH values are stored in the digging table and updated at each LP calculation.

## Slide 71: The Dynamic Assignment Layer
TKPH Remedies
Reduce tire load that trucks carry.
Reduce average traveling speed (lock truck in lower gear).
Reduce haul travel distance or put trucks on shorter hauls.
Use tyres with high TKPH ratings (out of controllers’ power).
Note: Mine controllers must keep the TKPH view open and monitored throughout the shift if TKPH is used in truck assignments and potential long hauls (TSF) exist in the mine.
Notes: Of these options above, the most common approach is to reduce travel speed.
Reducing speed by 10% will reduce TKPH by 10% and only reduce mine productivity by 10%, whereas a 20% reduction in payloads might be required to achieve a 10% TPKH reduction.
Jigsaw TKPH feature is used to improve productivity by maximizing material movements while minimizing the total amount of hauling by the trucks.
This feature tends to assign trucks with higher TKPH to shorter hauls however this is not a guarantee that the new assignment will reduce the TKPH value.
It highly advisable for Mine controllers to keep the TKPH view open and monitored throughout the shift if TKPH is used in truck assignments and potential long hauls exist in the mine.

## Slide 72
Thank you.
Notes: Thank you.